## Slide 1
M10: Explainable AI for Pile Stiffness Prediction
How does the model know which soil parameters matter?
A practical guide for civil engineering researchers
THE PROBLEM
Typhoon loads degrade soil stiffness around monopile foundations
THE MODEL
A Slot-Attention AI predicts KL, KR, KLR degradation curves
THE XAI
Three methods reveal WHY the model makes each prediction

## Slide 2
What Does M10 Do?
From 8 soil/pile measurements to 21-step stiffness degradation curves + explanations
INPUT: 8 Parameters
PI (Plasticity Index)
Gmax (Max Shear Modulus)
v (Poisson's Ratio)
Dp (Pile Diameter)
Tp (Wall Thickness)
Lp (Pile Length)
Ip (Moment of Inertia)
Dp/Lp (Slenderness)
M10: SwiGLU Slot-Attention Model
Feature Embedding
8 numbers --> 64-dim vector
21 Slots Initialised
1 initial + 20 drop slots
Cross-Attention (x3)
Slots query the input
Self-Attention (x3)
Slots share information
SwiGLU MLP (x3)
Each slot refines itself
Prediction Heads
Slot --> KL, KR, KLR values
OUTPUT: Stiffness Curves
KL
Lateral Stiffness
21 values showing how KL drops with cyclic loading
KR
Rotational Stiffness
21 values showing how KR drops with cyclic loading
KLR
Coupled Stiffness
21 values showing how KLR changes with cyclic loading

## Slide 3
What Are Slots?
The 21 internal states that represent different stages of stiffness degradation
Slots = Internal Representation States
The model uses 21 slots to represent the pile's condition:
Slot 1 = Initial state (before any loading)
Captures the pile's original stiffness (KL0, KR0, KLR0)
Slots 2-21 = Drop states (progressive degradation)
Each slot represents one step of stiffness reduction
Step 2 = small load ... Step 21 = extreme loading
Key Design: Physics-Consistent Constraints
KL and KR can only decrease (soil gets weaker)
KLR magnitude can only increase (coupling grows)
This is enforced in the model architecture itself
Prototype Compression:
20 drop slots are built from only 4 prototypes
Reduces parameters while preserving accuracy
21 Slots - Visual Layout
S1
Initial
Drop Slots (Degradation Steps)
S2
Drop 1
S3
Drop 2
S4
Drop 3
S5
Drop 4
S6
Drop 5
S7
Drop 6
S8
Drop 7
S9
Drop 8
S10
Drop 9
S11
Drop 10
S12
Drop 11
S13
Drop 12
S14
Drop 13
S15
Drop 14
S16
Drop 15
S17
Drop 16
S18
Drop 17
S19
Drop 18
S20
Drop 19
S21
Drop 20
Proto A
Proto B
Proto C
Proto D
Each colour = one prototype cluster. 20 drop slots are built from just 4 learned prototypes.

## Slide 4
The 3 Iteration Cycle
The model refines its predictions by repeating three operations three times
Iteration 1
CROSS-ATTENTION
Slots read the input data
Each slot queries the 8 soil/pile parameters to extract relevant info
SELF-ATTENTION
Slots communicate with each other
Slots share information to capture interactions (e.g. PI affects Gmax effect)
SwiGLU MLP
Each slot processes independently
Non-linear transformation refines each slot's internal representation
Iteration 2
CROSS-ATTENTION
Slots read the input data
Each slot queries the 8 soil/pile parameters to extract relevant info
SELF-ATTENTION
Slots communicate with each other
Slots share information to capture interactions (e.g. PI affects Gmax effect)
SwiGLU MLP
Each slot processes independently
Non-linear transformation refines each slot's internal representation
Iteration 3
CROSS-ATTENTION
Slots read the input data
Each slot queries the 8 soil/pile parameters to extract relevant info
SELF-ATTENTION
Slots communicate with each other
Slots share information to capture interactions (e.g. PI affects Gmax effect)
SwiGLU MLP
Each slot processes independently
Non-linear transformation refines each slot's internal representation
WHY 3 ITERATIONS? Each pass refines the slot representations. Iteration 1 captures basic features. Iteration 2 captures interactions. Iteration 3 fine-tunes for accurate stiffness degradation curves.

## Slide 5
Why Do We Need Explainability (XAI)?
AI models are powerful but opaque -- civil engineers need to trust and understand predictions
WITHOUT XAI
8 Soil/Pile Parameters
??? BLACK BOX
KL, KR, KLR Curves
X Cannot verify if predictions are physically reasonable
X No way to identify which soil parameter drives the result
X Cannot detect when the model is extrapolating dangerously
X Regulators and reviewers won't accept unexplained AI
X Engineers cannot build intuition from black-box outputs
WITH M10 XAI
8 Soil/Pile Parameters
GLASS BOX
KL, KR, KLR + WHY
+ See which soil parameters control each stiffness variable
+ Track how information flows through the model's internal states
+ Verify that the model learned real soil mechanics relationships
+ Build confidence for peer review and regulatory acceptance
+ Identify edge cases where the model may be unreliable

## Slide 6
M10 Uses Three Complementary XAI Methods
Each method answers a different question about the model's decision process
Cross-Attention Rollout
QUESTION:
Which slots are most active for this scenario?
HOW:
Tracks how much each of the 21 slots reads from the input soil parameters, averaged across all 3 iterations.
Output: 21 importance scores (one per slot, sum = 1.0)
SLOT-LEVEL TRANSPARENCY
Self-Attention Rollout
QUESTION:
How do the slots communicate internally?
HOW:
Tracks the information flow between all 21 slots across 3 iterations, accounting for residual connections.
Output: 21x21 flow matrix showing slot-to-slot influence
INTERACTION TRANSPARENCY
Gradient x Input (+ Integrated Gradients)
QUESTION:
Which of the 8 input features matters most for the prediction?
HOW:
Computes how much each soil/pile parameter contributes to each predicted stiffness value at each degradation step.
Output: importance score for each of the 8 input features
FEATURE-LEVEL TRANSPARENCY

## Slide 7
Cross-Attention Rollout: How Slots Read the Input
Visualising which of the 21 slots extract the most information from the soil parameters
INPUT
EMBEDDING
PI
Gmax
v
Dp
Tp
Lp
Ip
D/L
CROSS-ATTENTION
x 3 Iterations
Iter. 1: Initial read
S1: 0.05 S2: 0.04 S3: 0.06 ... S21: 0.05
Iter. 2: Refined read
S1: 0.05 S2: 0.04 S3: 0.06 ... S21: 0.05
Iter. 3: Final read
S1: 0.05 S2: 0.04 S3: 0.06 ... S21: 0.05
ROLLOUT RESULT
Average across 3 iterations, normalised to sum = 1.0
S1
S2
S3
S4
S5
S6
S7
S8
S9
S10
S11
S12
S13
S14
S15
S16
S17
S18
S19
S20
S21
What does this tell a civil engineer?
- High bar = that slot is actively reading the soil parameters to make its prediction
- Low bar = that slot relies more on information shared from other slots (self-attention)
- Slot 1 (initial stiffness) typically has high cross-attention because initial values depend directly on soil properties

## Slide 8
Self-Attention Rollout: How Slots Communicate
Tracking information flow between the 21 internal states across all iterations
How It Works
In each iteration, every slot can attend to every other slot.
This creates a 21x21 weight matrix per iteration.
The Residual Connection:
The model adds the slot's own previous state back in:
new_slot = LayerNorm( old_slot + attention_output )
This means ~50% of information is kept from before.
The Rollout:
We mix 50% identity + 50% attention at each iteration,
then multiply the three matrices together:
R = (0.5*I + 0.5*A3) x (0.5*I + 0.5*A2) x (0.5*I + 0.5*A1)
What civil engineers learn:
- Which degradation steps influence which other steps
- Whether early loading stages affect late-stage predictions
- The model's internal representation of progressive failure
Self-Attention Rollout Heatmap [21 x 21]
Brighter = stronger information flow from column slot to row slot
S1
S1
S3
S3
S5
S5
S7
S7
S9
S9
S11
S11
S13
S13
S15
S15
S17
S17
S19
S19
Source Slot (Key)
Reading the Heatmap:
Bright diagonal = each slot retains its own information (residual connection)
Bright off-diagonal = strong communication between those slots
Bright first row/column = initial slot influences or is influenced by all others

## Slide 9
Feature Attribution: Which Soil Parameters Matter Most?
Gradient x Input (fast) and Integrated Gradients (precise) trace predictions back to the 8 inputs
How Feature Attribution Works
Both methods answer: 'If I change this soil parameter slightly,
how much does the predicted stiffness change?'
Gradient x Input (Default -- ~50 ms):
Takes one snapshot: multiply each feature value by its gradient
Integrated Gradients (Precise -- ~2 sec):
Traces a path from 'no soil' to 'actual soil', averaging gradients
Guarantees all attributions sum exactly to the predicted value
Typical Feature Importance Result
(% contribution to prediction)
PI
28.5%
Gmax
24.2%
Lp
15.8%
Dp/Lp
11.3%
Ip
8.1%
Dp
5.6%
Tp
4.2%
v
2.3%
Feature Attribution Heatmap: [3 variables x 21 steps x 8 features]
For each stiffness variable:
KL (Lateral)
PI
Gmax
v
Dp
Tp
Lp
Ip
D/L
Step 1 --> Step 21
KR (Rotational)
PI
Gmax
v
Dp
Tp
Lp
Ip
D/L
Step 1 --> Step 21
KLR (Coupled)
PI
Gmax
v
Dp
Tp
Lp
Ip
D/L
Step 1 --> Step 21
RED = positive influence (pushes stiffness up) BLUE = negative influence (pushes stiffness down)
BRIGHTER = STRONGER influence on the prediction

## Slide 10
Summary: Three Perspectives on Model Transparency
Each method reveals a different aspect of how the model makes stiffness predictions
Cross-Attention Rollout
QUESTION
Which slots are most active for this scenario?
WHAT YOU SEE
A bar chart showing the importance of each of the 21 slots in reading the input
CIVIL ENG. VALUE
Identifies which degradation stages depend most directly on soil properties
Speed: < 1 ms
Self-Attention Rollout
QUESTION
How do degradation stages influence each other?
WHAT YOU SEE
A 21x21 grid (heatmap) showing information flow between all slot pairs
CIVIL ENG. VALUE
Reveals internal coupling: e.g. early loading stages affecting late-stage stiffness
Speed: < 1 ms
Feature Attribution
QUESTION
Which of the 8 soil/pile parameters drives each prediction?
WHAT YOU SEE
Ranked bar chart of feature importance + colour-coded heatmap across all steps
CIVIL ENG. VALUE
Directly answers: 'Is PI or Gmax more important for this specific pile scenario?'
Speed: 50 ms / 2 sec
All three methods are available in the M10 Web Dashboard. Select any test scenario and the XAI results are computed in real-time.