## Slide 1
M7 vs M8 vs M9
A Visual & Simple Guide to the Three Model Versions
M7 - Baseline
Parameters: 55,770
Accuracy (R2): 0.9897
M8 - Efficient
Parameters: 45,486
Accuracy (R2): 0.9882
M9 - SwiGLU (Best)
Parameters: 45,502
Accuracy (R2): 0.9915
What are these models?
They all predict how a pile (foundation) degrades over time.
Each version uses a smarter "brain" (MLP) to get more accurate with fewer parameters.
PFE - M7 / M8 / M9 Visual Comparison

## Slide 2
What Does the Model Do?
A simple explanation of the input, the brain, and the output
INPUT
8 numbers describing the pile:
Soil type (PI)
Soil stiffness (Gmax)
Soil ratio (v)
Pile diameter (Dp)
Pile thickness (Tp)
Pile length (Lp)
Pile flexibility (Ip)
Shape ratio (Dp/Lp)
Think of it as: describing the
pile and the ground around it.
THE BRAIN (Psi-NN)
1. Reads the 8 numbers
2. Splits them into "slots"
(like memory boxes)
3. Each slot learns a pattern
4. Combines slots to predict
how the pile changes
over 21 loading cycles
This is where M7/M8/M9 differ!
OUTPUT
3 curves over 21 time steps:
KL = Lateral stiffness
(side-to-side strength)
KR = Rocking stiffness
(tilting resistance)
KLR = Cross-coupling
(how KL and KR interact)
These curves show how the pile
gets weaker over time.
PFE - M7 / M8 / M9 Visual Comparison

## Slide 3
The 5 Building Blocks (All Versions Share This)
Each model has the same pipeline - the difference is in block 3 (the MLP)
1. Read Input
Turns 8 numbers
into 64 features
2. Slot Attention
Splits features
into memory slots
(like sorting info
into folders)
3. Slot MLP
Each slot goes
through a small
"brain" - THIS IS
WHAT CHANGES!
4. Rebuild Slots
Uses a recipe (R)
to reconstruct
all 21 time steps
from prototypes
5. Output
Produces the
3 curves:
KL, KR, KLR
The KEY difference between M7, M8, and M9:
M7 uses a BIG brain (wide MLP) for each slot -> lots of parameters, decent accuracy
M8 uses a SMALL brain (bottleneck MLP) for each slot -> fewer parameters, saves space
M9 uses a SMART brain (SwiGLU gated MLP) for each slot -> same small size, BEST accuracy
PFE - M7 / M8 / M9 Visual Comparison

## Slide 4
M7 Architecture (Drawn)
The baseline model - uses a wide MLP with 128 hidden neurons
M7 - Baseline
Input: 8 numbers
soil + pile properties
Embedding (8 -> 64)
expand to 64 features
Slot Attention (3 rounds)
7 slots: 1 initial + 6 prototypes
Wide MLP: 64 -> 128 -> 64
GELU activation | 16,512 params
Fixed Relation Matrix R
6 protos -> 20 drop-slots (frozen)
Output Head (64 -> 3)
KL, KR, KLR x 21 steps
Total: 55,770 params
How M7 Works (Simple)
1. Takes 8 input numbers about the pile and soil
2. Expands them to 64 features (like zooming in)
3. Slot Attention creates 7 "memory slots":
- 1 slot for initial state (time=0)
- 6 slots for typical degradation patterns
4. Each slot goes through a WIDE MLP (128 neurons)
This is a big brain - uses lots of parameters
Think: sledgehammer to crack a nut
5. A fixed recipe (R) builds 21 time steps from 6 patterns
Problem: this recipe can never improve!
6. Outputs KL, KR, KLR curves (how pile degrades)
Result: R2 = 0.9897 | Params: 55,770
PFE - M7 / M8 / M9 Visual Comparison

## Slide 5
M8 Architecture (Drawn)
3 upgrades: smaller MLP, learnable recipe, physics rules
M8 - Efficient
Input: 8 numbers
soil + pile properties
Embedding (8 -> 64)
expand to 64 features
Slot Attention (3 rounds)
6 slots: 1 initial + 5 prototypes
Bottleneck MLP: 64->48->64
GELU activation | 6,256 params
Learnable Relation R
5 protos -> 20 slots (adapts!)
Output + Physics Check
KL,KR must decrease / KLR increase
Total: 45,486 params
What Changed in M8 (3 Upgrades)
UPGRADE 1: Smaller MLP (bottleneck)
Old: 64 -> 128 -> 64 (16,512 params)
New: 64 -> 48 -> 64 ( 6,256 params) -62% smaller!
Like squeezing info through a narrow pipe
Forces the model to keep only what matters
UPGRADE 2: Learnable Recipe (R)
M7: recipe frozen after discovery -> can't improve
M8: recipe keeps learning during training -> adapts
Like a chef who keeps improving a recipe vs one who
writes it down once and never changes it
UPGRADE 3: Physics Rules
KL and KR MUST go down over time (pile gets weaker)
KLR MUST go up over time (coupling increases)
The model is penalized if it violates physics!
Result: R2 = 0.9882 | Params: 45,486 (19.7% smaller)
PFE - M7 / M8 / M9 Visual Comparison

## Slide 6
M9 Architecture (Drawn)
Uses SwiGLU - a smarter brain that decides what to focus on
M9 - SwiGLU (Best)
Input: 8 numbers
soil + pile properties
Embedding (8 -> 64)
expand to 64 features
Slot Attention (3 rounds)
6 slots: 1 initial + 5 prototypes
SwiGLU MLP (gated, dim=32)
gate decides what matters | 6,272p
Learnable Relation R
same as M8 (adapts)
Output + Physics Check
same physics rules as M8
Total: 45,502 params
What Changed in M9 (SwiGLU Brain)
THE KEY UPGRADE: SwiGLU replaces the plain MLP
Normal MLP (M7/M8):
Data goes in -> gets transformed -> comes out
Every feature is treated the same way
SwiGLU MLP (M9):
Data goes in through TWO paths:
Path 1 (Gate): decides "how important is this?"
Path 2 (Value): carries the actual information
The gate CONTROLS how much of each feature passes
Like a smart filter: amplifies useful info,
suppresses noise - without adding parameters
BONUS: Skips 2 training stages (reuses M8 results)
-> trains 2-3x faster!
Result: R2 = 0.9915 (BEST) | Params: 45,502
PFE - M7 / M8 / M9 Visual Comparison

## Slide 7
Side-by-Side Architecture Comparison
Same pipeline, different MLP brains - spot the differences!
M7
8 inputs
Embed 64
SlotAttn (7 slots)
Wide MLP 128
16,512 params
Fixed R (6 proto)
KL, KR, KLR
Total: 55,770 params
M8
8 inputs
Embed 64
SlotAttn (6 slots)
Bottleneck MLP 48
6,256 params
Learnable R (5 proto)
KL,KR,KLR + physics
Total: 45,486 params
M9
8 inputs
Embed 64
SlotAttn (6 slots)
SwiGLU MLP 32
6,272 params (gated)
Learnable R (5 proto)
KL,KR,KLR + physics
Total: 45,502 params
Shrink MLP
Add gating
PFE - M7 / M8 / M9 Visual Comparison

## Slide 8
The MLP Brain: How Data Flows Inside
This is THE most important difference between M7, M8, and M9
M7: Wide MLP
64 features
EXPAND to 128
GELU activation
COMPRESS to 64
Simple: everything goes through
a wide pipe. Uses 16,512 params.
M8: Bottleneck MLP
64 features
SQUEEZE to 48
GELU activation
EXPAND to 64
Narrow pipe forces compression.
Only 6,256 params (-62%).
M9: SwiGLU (Gated)
64 features
Gate path
SiLU(W_g * x)
Value path
W_v * x
MULTIPLY: gate x value
gate controls what passes
Output: 64 features
Smart filter: gate decides what
matters. 6,272 params. BEST accuracy.
PFE - M7 / M8 / M9 Visual Comparison

## Slide 9
The Relation Matrix R: A Recipe for Time Steps
How do we go from 5-6 patterns to 21 time steps?
Think of it like this: we have 5 (or 6) typical "patterns" of how a pile degrades.
The Relation Matrix R is a RECIPE that mixes these patterns to create all 21 time steps.
Pattern 1
Pattern 2
Pattern 3
Pattern 4
Pattern 5
5 prototypes
RECIPE (R)
Step 1 = 80% P1 + 20% P2
Step 2 = 60% P1 + 40% P2
Step 3 = 50% P2 + 50% P3
...
Step 20 = 90% P5 + 10% P4
Each step is a mix
of the patterns
Relation Matrix (20 x 5)
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
... up to Step 20
Step 0 (initial)
Special slot for time=0 (healthy pile)
M7: Recipe is FIXED (never changes)
-> like cooking with a rigid recipe
M8/M9: Recipe LEARNS during training
-> like a chef who keeps improving
-> gets better over time!
PFE - M7 / M8 / M9 Visual Comparison

## Slide 10
Physics Rules: Teaching the Model Real-World Behavior
M8 and M9 enforce physical laws - M7 does not
KL (lateral stiffness)
Side-to-side strength
Time 1: ████████████
Time 5: █████████
Time 10: ██████
Time 15: ████
Time 21: ██
KR (rocking stiffness)
Tilting resistance
Time 1: ████████████
Time 5: █████████
Time 10: ██████
Time 15: ████
Time 21: ██
KLR (cross-coupling)
How KL and KR interact
Time 1: ██
Time 5: ████
Time 10: ██████
Time 15: █████████
Time 21: ████████████
Why does this matter?
In the real world, piles ALWAYS get weaker over time.
The stiffness KL and KR always decrease.
The coupling KLR always increases.
Without physics rules, the model might predict
impossible results (like a pile getting STRONGER).
Which models enforce physics?
M7: NO physics rules
(might produce impossible curves)
M8: YES - physics penalty in loss function
(penalized if curves go wrong direction)
M9: YES - same physics rules as M8
PFE - M7 / M8 / M9 Visual Comparison

## Slide 11
How Each Model is Trained
M9 is much faster because it reuses work already done by M8
Stage A: Learn from Teacher
A student model copies the
teacher (M6) behavior.
Like a student copying notes.
Takes ~2,000 training rounds.
Stage B: Discover Patterns
Find k* typical patterns in
the student's memory slots.
Uses K-means clustering.
Discovers R matrix recipe.
Stage C: Final Training
Train the compact model with
k* slots and the R recipe.
Takes ~2,500 training rounds.
This is the final model!
 | Stage A (copy teacher) | Stage B (find patterns) | Stage C (final training) | Total time
M7 | YES (2,000 rounds) | YES (k*=6 found) | YES (2,500 rounds) | ~4,500 rounds
M8 | YES (2,000 rounds) | YES (k*=5 found) | YES (2,500 rounds) | ~4,500 rounds
M9 | SKIP (reuses M8) | SKIP (reuses M8) | YES (2,500 rounds) | ~2,500 rounds!
M9 is 2-3x faster because it reuses M8's Stage A and B results - no need to redo work!
PFE - M7 / M8 / M9 Visual Comparison

## Slide 12
Accuracy Comparison: Who Predicts Best?
R2 = how well the model fits (1.0 = perfect) | RMSE = prediction error (lower = better)
Chart: 
| M6 (Teacher) | M7 | M8 | M9
R2 | 0.98036 | 0.98966 | 0.98822 | 0.99151
R2 Score (higher = better)
Chart: 
| M6 (Teacher) | M7 | M8 | M9
RMSE (billions) | 29.7742 | 21.6004 | 23.0569 | 19.5792
Error in billions (lower = better)
PFE - M7 / M8 / M9 Visual Comparison

## Slide 13
Output Quality Per Variable: KL, KR, KLR
How well does each model predict each stiffness curve?
Chart: 
| M6 | M7 | M8 | M9
KL R2 | 0.97681 | 0.99098 | 0.98878 | 0.98951
Chart: 
| M6 | M7 | M8 | M9
KR R2 | 0.96336 | 0.98071 | 0.97802 | 0.98416
Chart: 
| M6 | M7 | M8 | M9
KLR R2 | 0.96897 | 0.98598 | 0.98447 | 0.98647
KL (side-to-side)
KR (tilting)
KLR (coupling)
What this tells us:
KL: M7 is slightly best (0.9910) but all are very close
KR: M9 is best (0.9842) - this is the hardest variable to predict
KLR: M9 is best (0.9865) - SwiGLU helps most on difficult variables
All student models beat the M6 teacher on every variable!
PFE - M7 / M8 / M9 Visual Comparison

## Slide 14
Model Size: How Many Parameters?
Fewer parameters = smaller model = faster to run = less memory needed
M6 (Teacher)
56,646 params
0% (reference)
M7
55,770 params
1.5% smaller
M8
45,486 params
19.7% smaller
M9
45,502 params
19.7% smaller
M8 and M9 are nearly the same size (only 16 params difference!) but M9 is more accurate thanks to smarter SwiGLU gating.
PFE - M7 / M8 / M9 Visual Comparison

## Slide 15
Where Do the Parameters Live?
The MLP is where M8/M9 saved most space
Chart: 
| M6 (Teacher) | M7 | M8 | M9
Slot MLP (the brain) | 16512 | 16512 | 6256 | 6272
Slot Attention | 20864 | 20864 | 20864 | 20864
Other (embed, init, output) | 2135 | 1239 | 1275 | 1275
Reading the chart:
The Slot MLP (orange/top section) is where
M8 and M9 saved the most space:
M6/M7: MLP = 16,512 params (huge!)
M8: MLP = 6,256 params (-62%)
M9: MLP = 6,272 params (-62%)
Slot Attention (middle) stays the same
in all models - it's already efficient.
The MLP was the "fat" part of the model.
M8 put it on a diet (bottleneck).
M9 made it smarter instead (SwiGLU).
PFE - M7 / M8 / M9 Visual Comparison

## Slide 16
Where Does M9 Struggle? (Worst Cases)
Most predictions are excellent, but a few edge cases are harder
Chart: 
| Scenario 56 | Scenario 141 | Scenario 73 | Scenario 84 | Scenario 60 | Scenario 137
Average Error % | 34.35 | 25.313 | 22.412 | 13.263 | 13.104 | 12.34
What This Means
204 test scenarios evaluated
Average error: only 2.37%
Median error: only 1.36%
Most predictions are very accurate!
A few extreme pile configurations
(unusual soil + pile combos) are harder.
Scenario 56 is the worst (34% error).
Overall M9 Quality:
Average accuracy (R2): 0.9829 -> Very good (close to 1.0 = perfect)
Average error (MAPE): 2.37% -> Very low (close to 0% = perfect)
95th percentile error: 6.28% -> Even worst 5% are below 6.3%
PFE - M7 / M8 / M9 Visual Comparison

## Slide 17
All Differences at a Glance
A simple comparison of everything that changed between M7, M8, and M9
What | M7 | M8 | M9
MLP brain type | Wide (big) | Bottleneck (small) | SwiGLU (smart)
MLP brain size | 128 neurons | 48 neurons | 32 neurons (x2 paths)
MLP parameters | 16,512 | 6,256 | 6,272
Has feature gating? | No | No | Yes (the key advantage)
Recipe (R) type | Fixed (frozen) | Learns during training | Learns during training
Number of patterns | 6 prototypes | 5 prototypes | 5 (reused from M8)
Physics rules? | No | Yes (penalty if wrong) | Yes (same as M8)
Training stages | A + B + C (slow) | A + B + C (slow) | C only (fast!)
Total parameters | 55,770 | 45,486 | 45,502
Size vs teacher M6 | 1.5% smaller | 19.7% smaller | 19.7% smaller
Accuracy (R2) | 0.9897 | 0.9882 | 0.9915 BEST
Error (RMSE x1e9) | 21.6 | 23.1 | 19.6 BEST
PFE - M7 / M8 / M9 Visual Comparison

## Slide 18
The Winner: M9
Best accuracy, nearly same size, and fastest to train
M9 - SwiGLU Psi-NN
Accuracy (R2): 0.9915
Parameters: 45,502
Compression: 19.7%
Training: Stage C only (fast!)
Best accuracy of all versions
Nearly same size as M8
2-3x faster to train
Enforces physics rules
Accuracy
M9 wins
Size
M8 wins (by 16)
Speed
M9 wins (3x)
Physics
M8 = M9
PFE - M7 / M8 / M9 Visual Comparison

## Slide 19
Summary: The Evolution
M7 -> M8 -> M9: each version gets smarter, not bigger
M7 (Baseline):
Uses a big wide brain (MLP with 128 neurons) and a fixed recipe.
Works well but wastes parameters. Only 1.5% smaller than teacher.
M8 (Efficient):
Shrinks the brain (48 neurons = 62% less), makes recipe learnable,
adds physics rules. 19.7% smaller than teacher. Smart compression.
M9 (SwiGLU - Best):
Replaces the brain with a gated version (SwiGLU).
The gate decides which features matter - like a smart filter.
Same small size as M8, but BETTER accuracy (0.9915 vs 0.9882).
Skips 2 training stages -> trains 2-3x faster.
Bottom line: M9 is the best model. Use it.
PFE - M7 / M8 / M9 Visual Comparison