## Slide 1
M9 → M10
Adding Explainable AI to the Physics-Informed Digital Twin
How does the model decide? Which input features matter? Where does information flow inside the network?
Layer-wise Relevance Propagation (LRP)
Traces each prediction back to the 8 soil/pile inputs
Attention Rollout
Maps the flow of information through cross & self attention
Token Attribution Maps
Visualises which features drive each degradation step
Pile Stiffness Degradation under Cyclic Loading — SwiGLU Slot-Attention Ψ-NN
Youssef Khalil • Shenzhen University / EMSI • 2026

## Slide 2
The Base Model: SwiGLU Ψ-NN (M9, unchanged in M10)
Understanding the architecture is the first step to explaining its predictions
8 Soil & Pile Inputs
▸ PI (Plasticity Index)
▸ Gmax (Shear Modulus)
▸ ν (Poisson Ratio)
▸ Dp, Tp, Lp (Geometry)
▸ Ip (Moment of Inertia)
▸ Dp/Lp (Slenderness)
Embedding
Transforms 8 numbers into a 64-dimensional representation the attention layers can process
Iterative Refinement ×3 rounds
Cross- Attention
Slots ask: 'What input info do I need?'
Self- Attention
Slots ask: 'What do other slots know?'
SwiGLU MLP
Decides which information to keep or discard
Predictions
KL — Lateral stiffness KR — Rotational stiffness KLR — Coupled stiffness 21 degradation steps for each variable
What are 'Slots'?
The model uses 21 slots — think of them as 21 specialised workers: ▸ Slot 1 is the 'initial condition' worker — predicts starting stiffness ▸ Slots 2–21 are 'degradation' workers — each one predicts how much stiffness drops at that step of the cyclic loading process
These slots don't work independently — they communicate through: ▸ Cross-attention: 'Let me check the soil properties again' ▸ Self-attention: 'What did the other degradation steps learn?' ▸ SwiGLU gating: 'I'll keep the relevant info, discard the noise'
M9 → M10: Same model, new power — Explainability
M9 was a black box — it made accurate predictions but couldn't explain WHY. M10 adds an XAI layer that looks inside the attention mechanism and traces predictions back to inputs. No model retraining needed. Same weights, same accuracy. We simply observe and explain.

## Slide 3
Layer-wise Relevance Propagation (LRP)
Tracing the model's prediction back to the 8 raw input features
The Big Idea
Imagine the model predicts KL = 5.2×10⁹ at step 10. LRP asks: 'How much did each input feature contribute to this specific number?' It works by computing how sensitive the output is to each input, then weighting by the input's actual value: Relevance of feature j = (input value) × (sensitivity)
How It Flows
PI
Gmax
ν
Dp/Lp
Ψ-NN Model (black box)
KL at Step 10 = 5.2 × 10⁹
← Relevance flows backward
What LRP Reveals
73%
Dp/Lp (Slenderness)
14%
Gmax (Shear Modulus)
4.4%
Ip (Moment of Inertia)
4.0%
Lp (Pile Length)
2.0%
PI (Plasticity Index)
1.3%
Tp (Wall Thickness)
0.8%
ν (Poisson Ratio)
0.5%
Dp (Pile Diameter)
← KL variable
Key Insight: LRP produces a 3D attribution map
For every combination of (variable × step × feature), we get a relevance score. That means 3 variables × 21 steps × 8 features = 504 individual attributions per scenario. This tells us not just WHICH features matter overall, but HOW they change across the degradation process.

## Slide 4
LRP Implementation: Gradient × Input
A simple yet powerful method that satisfies the conservation axiom
The Core Formula
Relevance of feature j = xⱼ × ∂ output / ∂ xⱼ
input value how much the output changes when this input changes slightly
Component 1: The Gradient ∂ŷ/∂xⱼ
The gradient measures sensitivity — if we nudge input feature j by a tiny amount, how much does the prediction change? ▸ Large gradient → model is very sensitive to this feature ▸ Small gradient → changing this feature has little effect ▸ Sign tells direction: positive means feature pushes prediction up, negative means it pushes it down
Component 2: The Input Value xⱼ
Multiplying by the input value is crucial because: ▸ A feature might have high sensitivity (large gradient) but its actual value is near zero → low real contribution ▸ Conversely, a moderate gradient on a large input value means significant actual contribution to the prediction ▸ This product captures the TRUE relevance of each feature
The Conservation Principle
Sum of all feature relevances ≈ the model's prediction (first-order Taylor approximation)
This means relevance is not artificially created or lost — the total amount of 'importance' distributed across the 8 features equals the model's output. Every feature gets its fair share.

## Slide 5
Attention Rollout: Cross-Attention
How much does each slot pay attention to the input features?
Input Embedding
The 8 soil/pile features compressed into one 64-dim vector (single token)
21 Slots
Slot 1
Slot 2
Slot 3
Slot 4
Slot 5
...
What Cross-Attention Shows
Each of the 21 slots sends a 'query' to the input embedding. The attention weight tells us how strongly that slot requested information. ▸ Thick arrow = high attention (slot heavily depends on input features) ▸ Thin arrow = low attention (slot is more self-sufficient) ▸ This happens 3 times (3 iterations), and we average the results
Rollout Across 3 Iterations
Iteration 1
+
Iteration 2
+
Iteration 3
+
Rollout (Average)
Each iteration produces attention weights for all 21 slots → we average them → normalise so they sum to 1
What Question Does Cross-Attention Rollout Answer?
"Which degradation steps are most influenced by the original soil/pile properties?" A slot with high cross-attention is heavily shaped by the input features. A slot with low cross-attention relies more on what other slots communicated to it. This reveals whether early, middle, or late degradation steps are input-driven vs. context-driven.

## Slide 6
Attention Rollout: Self-Attention
How do slots communicate with each other? Which degradation steps exchange information?
Slot-to-Slot Communication
Self-attention creates a 21 × 21 matrix: each cell (i, j) tells us how much Slot i listens to Slot j. This reveals temporal dependencies in the degradation process.
S1 S2 S3 S4 S5 S6 S7
S1
S2
S3
S4
S5
S6
S7
Brighter = stronger attention
Residual Mixing: The Key Innovation
In the real network, each slot keeps a copy of its own information (residual connection). We must account for this when rolling up across iterations. The formula: Mixed Attention = 50% × Identity + 50% × Attention ▸ The Identity part means: 'I keep half of my own information' ▸ The Attention part means: 'I take half from what other slots say' Then we multiply across all 3 iterations: Rollout = Mixed₃ × Mixed₂ × Mixed₁ This matrix multiplication traces the TOTAL flow of information from source slots to destination slots across the entire network.
Why Separate Cross and Self Attention?
Cross-Attention Rollout
Shape: 21 values (one per slot) Answers: "How strongly does each degradation step depend on the original soil/pile inputs?" Interpretation: input-driven vs. context-driven behaviour
Self-Attention Rollout
Shape: 21 × 21 matrix (slot-to-slot) Answers: "Which degradation steps influence each other? Does step 15 look at step 3 for guidance?" Interpretation: temporal coupling in the degradation process

## Slide 7
Token Attribution Maps: The Complete Picture
Combining LRP and Attention Rollout into an interactive visualisation
The Attribution Heatmap
A colour-coded grid showing the relevance of each feature at each degradation step:
Step 1 Step 2 Step 3 Step 4 ... Step 21
PI
Gmax
ν
Dp
Tp
Lp
Ip
Dp/Lp
■ Intense red = high positive relevance ■ Light = low relevance
How to Read the Map
Each cell answers a specific question:
▸ Row = which feature
PI, Gmax, ν, Dp, Tp, Lp, Ip, Dp/Lp
▸ Column = which step
Step 1 (initial) through Step 21
▸ Colour = how important
Red = pushes prediction up, Blue = pushes down
▸ Intensity = magnitude
Darker = stronger influence
▸ Switchable by variable
Show heatmap for KL, KR, or KLR
▸ Per-scenario
Each test scenario generates its own attribution map
▸ Interactive
Hover over any cell to see the exact relevance value
The XAI Dashboard: Three Complementary Views
Feature Attribution Heatmap
8 features × 21 steps with red/blue colour coding Switchable: KL / KR / KLR
Cross-Attention Bar Charts
21 bars per iteration (×3) + averaged rollout chart Taller = more input-dependent
Self-Attention Heatmaps
21 × 21 matrix per iteration + multiplicative rollout Brighter = stronger connection

## Slide 8
Integrated Gradients: The Gold Standard
A more rigorous version of LRP that guarantees perfect conservation
The Intuition: Walking the Path
Imagine a hiker walking from point A (all inputs = 0) to point B (actual input values). At each step of the walk, they measure the gradient: 'which direction is uphill?' Integrated Gradients averages these measurements across the entire walk — not just at the destination. This gives a more complete picture than Gradient × Input, which only measures the gradient at point B.
The Formula (Simplified)
Attribution of feature j =
(xⱼ − 0) × average gradient along the path
We split the path into 30 equal steps, compute the gradient at each step, average them, then multiply by the input value. This guarantees:
Σ (all attributions) = f(x) − f(baseline) exactly
Gradient × Input vs Integrated Gradients
Gradient × Input (Default)
▸ Speed: ~50 ms per scenario — instant
▸ Accuracy: First-order approximation (very good)
▸ Conservation: Approximate — sum ≈ prediction
▸ When to use: Interactive dashboard (fast exploration)
▸ Gradient calls: 63 per scenario (3 vars × 21 steps)
Integrated Gradients (Gold Standard)
▸ Speed: ~2 seconds per scenario — slower
▸ Accuracy: Exact path integral (provably correct)
▸ Conservation: Exact — sum = prediction − baseline
▸ When to use: Research publications, formal analysis
▸ Gradient calls: 1,890 per scenario (30× more)

## Slide 9
The Complete M10 Pipeline
Same prediction model as M9 — with a new XAI observation layer (no retraining)
M9 Base (Unchanged)
Soil & Pile Parameters
8 inputs
Embedding Layer
8 → 64 dim
Cross-Attn (×3 iter.)
input → slots
Self-Attn (×3 iter.)
slot ↔ slot
SwiGLU MLP
gated filtering
Prediction Heads
slots → curves
M10 XAI Layer (NEW)
— observes the model's internal state, does not modify it
Cross-Attention Rollout
Captures attention weights from all 3 iterations. Averages → normalises. Result: 21-value vector (one importance score per degradation slot)
Self-Attention Rollout
Captures 21×21 attention matrices from each iteration. Mixes with 50% identity (residual connection). Multiplies across iterations. Result: 21×21 flow matrix
Gradient × Input (LRP)
Computes the gradient of each output w.r.t. each input feature. Multiplies by input value. Result: 3 × 21 × 8 tensor (var × step × feature)
Feature Importance
Sums absolute relevance across all 21 steps for each feature. Normalises to percentages. Result: 8 importance values per variable

## Slide 10
Summary: M9 → M10
MODEL RETRAINING
None
NEW DEPENDENCIES
Zero
MODEL ACCURACY
Unchanged
XAI METHODS
3 + Dashboard
LRP / Gradient × Input
What it answers: "How much does each soil/pile parameter contribute to each degradation step prediction?" Key findings: ▸ Dp/Lp (slenderness) dominates KL predictions at 73% ▸ Gmax is 2nd most important ▸ Attribution changes across steps ▸ Different for KL vs KR vs KLR
Attention Rollout
What it answers: "Where does information flow inside the model?" Two separate views: ▸ Cross: input → slot flow (which steps use input data?) ▸ Self: slot → slot flow (which steps talk to each other?) ▸ Residual mixing accounts for skip connections in the network
Token Attribution Maps
What it provides: "An interactive dashboard to explore explanations visually." Three linked panels: ▸ Feature × Step heatmap (red = positive, blue = negative) ▸ Cross-attention bar charts (one per iteration + rollout) ▸ Self-attention 21×21 heatmaps ▸ Per-scenario, per-variable
Why Does Explainability Matter?
A black-box model predicts KL will drop by 15% — but can we trust it? Should engineers act on it? XAI transforms trust: 'KL drops because Dp/Lp = 0.25 (slender pile) and Gmax = 23 MPa (soft soil) dominate this scenario, and the early degradation steps are heavily input-driven.' This is the difference between a number and a decision support system.