## Slide 1
M6 — Pile Stiffness Degradation Prediction
Slot-Attention Transformer · Physics-Informed · LSTM-Free
Architecture · Fine-tuning Strategy · MLP vs LSTM · Efficiency · Error Metrics
✓ Predict KL, KR, KLR over 21 steps
✓ 64.1% fewer parameters than M5
✓ Hard-coded monotonicity guarantees
PFE Project | April 2026

## Slide 2
Problem & Goal
Predicting pile-soil stiffness degradation under cyclic loading
Given 8 geotechnical input features, predict 3 stiffness quantities over 21 cyclic loading steps
INPUT (8 features) PI, Gmax, ν, Dp, Tp, Lp, Ip, Dp/Lp
M6 MODEL (Slot-Attention Transformer)
OUTPUT (21 × 3) KL(t), KR(t), KLR(t) for t = 1 … 21
21 Learnable Slots
One slot per degradation step — temporal structure without RNN
Physics Constraints
ΔKL, ΔKR ≤ 0 | ΔKLR ≥ 0 (hard-coded monotonicity)
Cumulative Sum
K(t) = K⁰ + Σ Δₙ — error never resets
Signed Log Scale
Handles mixed-sign targets (KLR < 0, KL/KR > 0)
Stiffness quantities: KL = lateral | KR = rotational | KLR = cross-coupling (always < 0, increases toward 0 under loading)
Data Pipeline
• 44 raw time steps → subsampled to 21 (equal spacing)
• Signed log transform: sign(y)·log(1+|y|) → preserves negative KLR
• RobustScaler per output variable (median/IQR, robust to outliers)
• Additive drop model: network learns Δ, not absolute K — physically motivated

## Slide 3
Architecture Overview
M6 — SlotAttentionDegradation (LSTM-free, physics-constrained)
INPUT [B, 8]
8 features
EMBEDDING Linear 8→64 LayerNorm GELU [B,1,64]
21 LEARNABLE SLOTS [B, 21, 64]
Slot 1 (initial) + Slots 2–21 (drops)
ITERATIVE SLOT REFINEMENT ×3
Cross-Attention Q=slots K=V=input
Add & LN
Self-Attention Q=K=V =slots
Add & LN
Slot MLP 64→128→64
Add & LN
Refined Slots [B, 21, 64]
Slot 1 (initial) [B,1,64]
Initial MLP 64→32→3 → K⁰
[B, 1, 3]
Slots 2–21 [B,20,64]
Drop MLP (shared) 64→32→3 → Δ drops
Physics Constraint −|Δ| for KL,KR ; +|Δ| for KLR

## Slide 4
Fine-Tuning Strategy
How M6 was trained from scratch and what was changed from M5
M6 is not a pretrained model fine-tuned from M5 — it is trained from scratch, but the training strategy was carefully redesigned based on M5's failure modes.
① Initial Loss Weighting ×5
• MSE on Slot 1 (initial K⁰) multiplied by 5.0
• Any error in K⁰ propagates forward via cumulative sum
• Forces the model to anchor the trajectory correctly first
• M5 used ×3 — M6 raises to ×5 (LSTM no longer corrects drift)
② Shape Loss (Huber on Δ)
• Penalises changes in consecutive drops: Huber(Δₜ − Δₜ₋₁)
• Encourages smooth degradation curves, not zigzag predictions
• Huber norm: robust to large isolated errors (vs pure L2)
③ Gradient Clipping & Scheduler
• Gradient clip = 2.0 (M5: 1.0) — relaxed to let early gradients flow
• ReduceLROnPlateau: patience 80 (M5: 100) — faster adaptation
• Early stopping patience 200 epochs (M5: 300)
④ Weight Decay & Normalisation
• Weight decay = 0.005 (M5: 0.01) — reduced to prevent over-regularisation
• RobustScaler on targets: median/IQR instead of mean/std
• Signed log transform preserves sign of cross-coupling term KLR
Total loss = MSE_overall + 5.0 × MSE_initial + λ_shape × ShapeLoss

## Slide 5
MLP vs LSTM Decoder
Why M6 replaced the LSTM with a direct per-slot MLP
M6 — Per-Slot MLP ✓
• Slots 2–21 as input
Each slot vector [64-dim] goes independently into the shared MLP
• Single forward pass
64 → 32 → 3 (GELU activation) — all 20 slots in parallel
• No hidden state
No sequential dependency between slots at decoding time
• Temporal structure from attention
3 rounds of cross + self-attention encode temporal order
• Physics applied after MLP
−|output| for KL, KR ; +|output| for KLR
• Cumsum reconstructs trajectory
K(t) = K⁰ + Σ Δₙ → absolute stiffness values
M5 — LSTM Decoder (removed in M6)
• Input: aggregated slot vector
Mean of all 21 slots → single [64-dim] context vector
• 2-layer LSTM unrolled 20 steps
Hidden state hₜ = LSTM(hₜ₋₁, context) — sequential
• Decoder cross-attention
Each LSTM step attends back to all refined slots
• Positional embeddings
Learnable pos_embed added to LSTM inputs for step identity
• h₀, c₀ projections
Separate MLPs to initialise LSTM hidden & cell states
• 101,312 extra parameters
seq_decoder + decoder_cross_attn + h0_proj + c0_proj + pos_embed
Key insight: self-attention already encodes temporal order through slot position — LSTM adds sequential decoding overhead but the ordering is already captured

## Slide 6
Efficiency Gains
M6 vs M5 — measured on identical hardware (CPU, batch=32)
157,958 → 56,646
Parameters
64.1% FEWER
632.7 KB → 231.2 KB
Model File Size
63.5% SMALLER
11.38 ms → 9.07 ms
Inference Time (CPU)
1.25× FASTER
Where did 101,312 parameters go?
Module Removed
Parameters
Purpose
seq_decoder (LSTM 2-layer)
66,176
Entire sequential decoder — largest chunk
decoder_cross_attn
16,640
Cross-attention between LSTM steps and slots
h0_proj + c0_proj
16,640
Linear projections to initialise LSTM hidden/cell state
pos_embed (learnable)
1,280
One embedding vector per step (20 × 64)
TOTAL REMOVED
100,736
TOTAL ADDED (3rd iteration reuses existing layers)
+0
Zero new params — only extra compute
The 3rd refinement iteration reuses the SAME cross-attention + self-attention + MLP layers — zero parameter cost, only extra forward-pass compute (~10 ms).

## Slide 7
Accuracy vs. Efficiency Trade-off
Full metric comparison M5 ↔ M6
M5 is more accurate on all metrics — M6 trades some accuracy for 64% fewer parameters and stronger physics guarantees.
Target
Metric
M5
M6
Δ (M6 − M5)
Overall
R²
0.9913
0.9804
−0.0109
Overall
RMSE
1.98 × 10¹⁰
2.98 × 10¹⁰
+51%
Overall
MAE
2.98 × 10⁹
3.33 × 10⁹
+12%
KL
R²
0.9907
0.9768
−0.0139
KL
RMSE
6.21 × 10⁷
9.79 × 10⁷
+58%
KR
R²
0.9838
0.9634
−0.0204
KR
RMSE
3.42 × 10¹⁰
5.15 × 10¹⁰
+51%
KLR
R²
0.9882
0.9690
−0.0192
KLR
RMSE
1.18 × 10⁹
1.92 × 10⁹
+63%
Slot 1→21
R² trend
0.9908→0.9968
0.9811→0.9809
M5 improves; M6 flat
Slot 1→21
RMSE trend
2.40×10¹⁰→2.69×10⁹
3.45×10¹⁰→6.57×10⁹
Both decrease (magnitudes shrink)
KR has the largest RMSE gap — rotational stiffness benefits most from LSTM's sequential context. KLR R² gap is large because the new +|Δ| constraint changes the output distribution.

## Slide 8
Error Metrics
R², RMSE, MAE — definitions, properties, and how to read them
R² (Coefficient of Determination)
R² = 1 − Σ(y−ŷ)² / Σ(y−ȳ)²
• Range: −∞ to 1.0 (1.0 = perfect fit)
• Scale-free: comparable across variables
• Negative R² → model worse than predicting the mean
• Best metric for slot-to-slot comparison
RMSE (Root Mean Square Error)
RMSE = √[ (1/n) Σ(y−ŷ)² ]
• Same physical units as the target (N, N·m…)
• Always ≥ 0 (squares → never negative)
• Penalises large errors heavily (squared term)
• Large values here reflect large stiffness magnitudes (10¹⁰)
MAE (Mean Absolute Error)
MAE = (1/n) Σ|y−ŷ|
• Same units as target, always ≥ 0
• Robust to outliers (no squaring)
• For same target: MAE ≤ RMSE always
• Easier to interpret physically
Granularity Levels
Overall
Flatten all N×21×3 predictions
Global model health check
Per-variable
Collapse time axis: N×21 per KL/KR/KLR
Which output is hardest?
Per-slot
Collapse variable axis: N×3 per step 1–21
Where on trajectory is error worst?
Per-scenario
One prediction of 21×3
Which input combinations fail?

## Slide 9
Understanding Errors Across 21 Slots
Why per-slot RMSE/MAE decrease ≠ better accuracy — use R²
Observed Pattern: RMSE and MAE both decrease from Slot 1 → 21
M5
Slot 1 RMSE = 2.40×10¹⁰ → Slot 21 RMSE = 2.69×10⁹ (Decrease: ~9×)
M6
Slot 1 RMSE = 3.45×10¹⁰ → Slot 21 RMSE = 6.57×10⁹ (Decrease: ~5×)
WHY this happens — two reasons:
① Physical magnitudes shrink: Stiffness degradation is larger in early cycles (big initial drops), so absolute errors in N or N·m are naturally larger at Slot 1 than Slot 21. RMSE and MAE are scale-dependent — they inherit this pattern.
② Cumulative sum drift: Early errors propagate forward (K(t) = K⁰ + Σ Δₙ), so Slot 1 carries the highest absolute burden. Later drops are smaller, so errors contributed per step are also smaller.
Use R² for slot comparison
• R² is scale-normalised — measures how much better the model is than predicting the mean
• For M5: Slot R² improves 0.9908 → 0.9968 ↑ (LSTM adds sequential context as trajectory progresses)
• For M6: Slot R² stays flat 0.9811 → 0.9809 → (no sequential memory — each slot predicted independently)
• This flat profile is M6's signature trade-off — uniform quality, no improvement over trajectory
Webapp: Percentage Error per Step — the most interpretable metric
Err% = |ŷ − y| / |y| × 100
Scale-independent: a 10% error at Slot 1 and Slot 21 are equally meaningful — unlike RMSE which is dominated by early-slot magnitudes.
■ < 5% Green (excellent)
■ 5–20% Orange (acceptable)
■ > 20% Red (poor)
Summary: which metric to use when?
Metric
Properties
Best used for
R²
Scale-free, 0–1
Slot-to-slot comparison, variable comparison, headline accuracy
RMSE
Physical units, ≥ 0
Absolue error magnitude; dominated by early slots / large-magnitude variables
MAE
Physical units, ≥ 0
Same as RMSE but more robust; physical interpretation
Err%
Percentage, ≥ 0
Webapp display; best for per-step human-readable quality check

## Slide 10
M6 — Summary
Simpler · Faster · Physics-Guaranteed · LSTM-Free
Architecture
21 learnable slots · 3× refinement (cross-attn → self-attn → MLP) · per-slot MLP prediction
vs M5
Removed LSTM decoder (101,312 params) · Added 3rd iteration · Added KLR sign constraint
Efficiency
64.1% fewer parameters · 63.5% smaller file · 1.25× faster inference
Accuracy
R² 0.9804 (vs 0.9913) · All three targets accurately predicted · KR largest gap
Physics
ΔKL ≤ 0, ΔKR ≤ 0, ΔKLR ≥ 0 hard-coded · Monotonicity structurally guaranteed
Metrics
R² best for slot comparison (scale-free) · RMSE/MAE in physical units (always ≥ 0)
M6 = M5 − LSTM + stronger constraints + 3 attention iterations

## Slide 11
What the Ψ-NN Paper Adds
Automatic structure discovery for physics-informed models
Paper: Liu et al. (Nature Communications, 2025) — Automatic network structure discovery of physics informed neural networks via knowledge distillation
Core innovation
1. Train a teacher network for physics accuracy first.
2. Train a student network with regularization, but without mixing that regularization into the physics loss.
3. Cluster learned weights and detect repeated, opposite, or permuted patterns.
4. Rebuild a smaller structured network with those rules hardwired.
Why it is physically interesting
The paper argues that PINNs usually enforce physics only through loss terms, not through internal wiring.
Ψ-NN tries to convert physical patterns into architecture rules: symmetry, sign reversal, permutation, parameter sharing.
That means the model can satisfy some constraints structurally at every forward pass, not only on average during training.
This is the same philosophy as your M6 sign constraints and cumulative-sum monotonicity.
Paper evidence
Claim
Paper result
Mechanism
Teacher/student staged optimization
Discovery
Clustering + parameter reconstruction
Physics encoded
Symmetry, anti-symmetry, conservation-style structure
Reported gain
~50% fewer iterations to same loss on Laplace
Reported gain
~95% lower final L2 error on Laplace vs PINN
Extra value
Transferability across PDE settings / parameters
Important: those exact gains come from PDE benchmarks, not from your pile dataset, so they support the idea but do not guarantee the same numbers for M6.

## Slide 12
How Ψ-NN Translates to Pile Physics
What physical structure could be discovered or hardwired in M6
The paper is about PDE symmetries, but the same idea can be translated to degradation physics: identify repeated physical patterns, then build them directly into the network.
Paper idea
Meaning in paper
Translation to M6 / pile degradation
Sign rule
Positive / negative parameter relations
Already used: ΔKL, ΔKR ≤ 0 and ΔKLR ≥ 0 are structural physics constraints
Shared prototypes
Many weights are copies of a small set
Drops across slots may come from a few degradation regimes: early, middle, late cycles
Permutation / symmetry
Different neurons are the same up to reordering
KL and KR may share partial structure under similar soil-pile response patterns
Relation matrix
Explicit rules between parameters
Could encode: slot j uses prototype p with scale αj, not a fully free head
Transferability
Structure survives parameter changes
A discovered slot structure may transfer across different PI, Gmax, Lp or loading scenarios
Reconstruction
Rebuild a smaller architecture
Replace many free slot-specific patterns by a smaller family of physically meaningful patterns
Most direct physics bridge
M6 already behaves like a small Ψ-NN idea: instead of only punishing bad physics in the loss, it hardwires monotonic degradation through sign constraints + cumulative sum.
Most innovative next step
Discover whether the 20 drop slots really need 20 independent behaviors, or whether they collapse into a few reusable physical prototypes with learned scaling rules.

## Slide 13
Can the Paper Make M6 More Efficient?
Yes — if used as structure-guided compression, not as blind pruning
Short answer: YES
The paper's strongest idea is not just adding more physics. It is using physics + distillation to compress a model while protecting accuracy.
Why it could help M6
M6 is already compact, so naive pruning may hurt accuracy.
Ψ-NN-style discovery would remove redundancy only after learning the task well.
That is better aligned with your objective: keep accuracy, compress only repeated structure.
What to try in this project
Teacher = current best M5 or M6 model.
Student = regularized compact slot model.
Then cluster slot/head weights and rebuild a smaller structured version.
Concrete efficiency ideas inspired by the paper
Idea
How to apply it
Why it may preserve accuracy
1. Prototype drop heads
Cluster the 20 slot-drop behaviors into 3–5 physical regimes (early / middle / late) and use one shared prototype per regime
Fewer free patterns, better interpretability, lower overfitting risk
2. Structured KL/KR coupling
Force partial weight sharing between KL and KR branches, with small correction terms
May keep accuracy because both are monotonic stiffness channels
3. Distilled M6-lite
Train a tiny student from current M6 predictions, then add the same sign/cumsum physics rules
Best chance to reduce size without losing much accuracy
4. Slot relation matrix
Represent some slot weights as scaled copies or sign-variants of prototype slots
Closer to the Ψ-NN reconstruction idea
5. Transfer by scenario family
Discover one structure on one soil/loading regime, reuse it on nearby regimes
Could reduce retraining cost and improve generalization
Best recommendation: use the paper as a second-stage compression method after training, not as a replacement for your current M6 training pipeline.
Expected outcome: moderate extra efficiency gains with smaller accuracy loss than manual simplification, but this needs experiments on your pile dataset because PDE symmetry results do not transfer one-to-one.

## Slide 14
Does the Method Understand Neuron Layering?
Yes: it analyzes each layer matrix and finds reusable neuron patterns
Simple answer: the method does not 'understand' like a human; it statistically detects repeated patterns in layer weights, then converts those patterns into architecture rules.
Layer-by-layer discovery (simple view)
1) Take one trained layer matrix W (for example, from a slot head).
2) Treat each row as one neuron's connection pattern.
3) Measure row similarity: same shape, opposite sign, or permuted order.
4) Cluster rows into groups: one prototype + relation rule.
5) Rebuild layer with fewer independent rows and explicit relations.
W (before)
Prototype + rules
p1
p2
row3 = -p1
row4 = perm(p2)
What this means for M6
• Drop MLP (64→32→3) can be analyzed neuron-by-neuron after training.
• If several hidden neurons behave almost the same, keep only one prototype neuron and map others by rules.
• If some slot behaviors are sign-flips/scaled copies, encode that explicitly instead of learning each slot independently.
• Result: fewer effective free parameters and more interpretable internal structure.
• Risk control: always validate on KR/KLR metrics, because these channels are most sensitive in your model.

## Slide 15
Graphical Architecture: M6 + Ψ-NN Compression
Practical pipeline to keep accuracy and improve efficiency
Use this as a two-stage engineering workflow: train for accuracy first, then discover and hardwire structure.
A) Teacher Strong baseline (M5 or current M6)
B) Student Compact model + regularization
C) Weight Analysis Cluster rows/neurons find relations
D) Rebuild Structured M6-lite (prototypes + rules)
E) Validate R², RMSE, MAE per variable + per slot
Inside the model (what changes and what stays)
Input + Embed 8→64
Slot Refinement Cross/Self/MLP ×3
Slot Heads Initial head + Drop head
Ψ-Extraction Prototype neurons + relation rules
Structured Heads smaller effective DoF
Keep physics hard constraints unchanged: ΔKL, ΔKR ≤ 0 and ΔKLR ≥ 0; cumsum reconstruction remains identical.
Part
Before
After Ψ-NN-style rebuild
Refinement block
Same
Same (no need to change)
Drop head behavior
Fully free
Prototype-constrained
Interpretability
Low
Higher (explicit relations)
Expected efficiency
Current
Better with controlled accuracy drop

## Slide 16
Worked Example: From 20 Drop Slots to 4 Prototypes
Detailed enough to understand, simple enough to explain
Goal: show how neuron/slot structure discovery can compress the model without changing the physics output logic.
Step-by-step example
1) Train baseline M6 normally (same losses and constraints).
2) Collect slot-drop latent vectors for slots 2..21 on validation set.
3) Cluster these 20 slots into 4 groups: early, early-mid, late-mid, late.
4) Learn 4 prototype drop mappings P1..P4 instead of 20 independent behaviors.
5) For each slot j, predict Δ using prototype Pk plus a tiny scalar adapter αj.
6) Keep sign constraints and cumulative sum exactly unchanged.
7) Compare old/new on per-variable per-slot RMSE and MAE.
Presentation sentence: 'We replace many free slot behaviors with a few physically reusable prototypes.'
Graphical mapping
Slots 2..21 (20 drop slots)
Cluster into 4 groups
P1
P2
P3
P4
slot j uses Pk with scale αj
Physics block −|ΔKL,ΔKR| , +|ΔKLR| then cumulative sum
Check
Accept if
Overall accuracy
R² drop is small (project-defined threshold)
KR stability
KR RMSE/MAE does not degrade sharply
KLR physics
Sign/monotonic behavior remains physically valid
Efficiency
Params and runtime improve enough to justify change