## Slide 1
M7 → M8
Efficient Ψ-NN: Architecture Upgrades & Physics Constraints
Pile Stiffness Degradation — M8 vs M7 Technical Comparison
M7 Params
55,770
M8 Params
45,486
Compression
19.7 %
Ψ-Model R²
0.9882
Three efficiency upgrades: Bottleneck MLP • Learnable Relation Matrix • Physics-Monotonic Loss
PFE Research · 2026

## Slide 2
Reminder: M7 — Ψ-NN Pile Stiffness Model
What we built in M7 before upgrading to M8
ARCHITECTURE
▸ 3-Stage pipeline: Distillation → Discovery → Ψ-Model
▸ Slot Attention: 64-dim, 4 heads, 3 iterations
▸ MLP per slot: 64 → 128 → 64 (wide bottleneck)
▸ 1 initial slot + 20 drop slots
▸ Fixed relation matrix R (from K-means, frozen)
▸ M6 teacher frozen for distillation (Stage A)
▸ K-Means Stage B: discovered k*=6 prototypes
M7 RESULTS
Ψ-Model Parameters
55,770
Compression vs M6
1.5 %
Ψ-Model R² (test)
0.9897
Ψ-Model RMSE
21.60 B
PER-VARIABLE R²
KL (lateral stiffness)
0.9910
KR (rotational stiffness)
0.9807
KLR (coupling)
0.9860
Loss = L_distill + L_seq + 5·L_initial + L_shape

## Slide 3
M8: Three Efficiency Upgrades at a Glance
All three upgrades are additive — M7 foundations remain intact
① Efficient Bottleneck MLP
Replace the wide slot MLP (64→128→64) with a narrow bottleneck (64→48→64) → ~40% fewer MLP params → EfficientSlotMLP class
② Learnable Relation Matrix
Convert the fixed buffer R (from K-means Stage B) into a learnable parameter via softmax logits → R evolves during training → Valid prob. distribution
③ Physics-Monotonic Loss
Add two new loss terms: • Relation-entropy (0.02×) • Monotonic penalty (0.2×) KL, KR ↓ over time KLR ↑ over time → Physically realistic curves
Combined effect: 19.7% compression vs M6 teacher · Physically constrained predictions

## Slide 4
Upgrade ① — EfficientSlotMLP (64 → 48 → 64)
Narrower bottleneck reduces parameters by ~40% with negligible accuracy loss
M7 — Wide MLP
64 → 128 → 64
M8 — EfficientSlotMLP
64 → 48 → 64
self.slot_mlp = nn.Sequential( nn.Linear(64, 128), # 8,192 params nn.GELU(), nn.Dropout(0.1), nn.Linear(128, 64), # 8,192 params ) # Total MLP: ~16,384 params
class EfficientSlotMLP(nn.Module): def __init__(self, d=64, btl=48): self.net = nn.Sequential( nn.Linear(d, btl), # 3,072 params nn.GELU(), nn.Dropout(0.1), nn.Linear(btl, d), # 3,072 params ) # Total MLP: ~6,144 params
PARAMETER COUNT COMPARISON
M6 Teacher
56,646
M7 Student
56,646
M7 Ψ-Model
55,770
M8 Student
46,326 ↓
M8 Ψ-Model
45,486 ↓

## Slide 5
Upgrade ② — Learnable Relation Matrix R
Fixed K-means initialisation → trainable parameter that adapts during Stage C
WHAT IS THE RELATION MATRIX?
▸ R is a [20 × k*] matrix (20 drop slots, k* prototypes)
▸ Each row = mixing weights for one time step
▸ Maps k* prototype slots → 20 degradation steps
▸ Stage B (K-means) provides a good initialisation
M7 (FIXED)
# register_buffer = NOT a learnable parameter self.register_buffer( 'relation_matrix', torch.FloatTensor(R) # frozen after Stage B )
M8 (LEARNABLE)
# nn.Parameter = gradient flows through R self.relation_logits = nn.Parameter( torch.log(R_init.clamp(min=1e-6)) ) # log-space for numerical stability def get_relation_matrix(self): # Row-softmax → valid prob distribution return torch.softmax( self.relation_logits, dim=1 )
BENEFITS
▸ R adapts to minimize the multi-objective loss
▸ Row-softmax ensures valid probability mix
▸ Entropy regularisation sharpens assignments
▸ Saved as relation_matrix (learned) in config

## Slide 6
Upgrade ③ — Physics-Monotonic Loss
Two new loss components enforce physically realistic pile degradation behaviour
PHYSICAL CONSTRAINTS
Pile stiffness under cyclic loading must satisfy:
KL (lateral stiffness)
↓ decreases (pile softens)
KR (rotational stiffness)
↓ decreases (pile softens)
KLR (coupling term)
↑ increases (coupling grows)
M7 had no explicit enforcement of these constraints → predictions could violate physical laws
M7 LOSS vs M8 LOSS
M7: L = L_distill + L_seq + 5·L_initial + L_shape
M8: L = L_distill + L_seq + 5·L_initial + L_shape + 0.02·L_rel_entropy + 0.2·L_mono_physics
M8 IMPLEMENTATION
# Physics-monotonic penalty diff_kl_kr = psi_out[:,1:,:2] - psi_out[:,:-1,:2] diff_klr = psi_out[:,1:,2:] - psi_out[:,:-1,2:] # Penalise violations: loss_mono = ( torch.relu(diff_kl_kr).mean() # KL,KR must NOT increase + torch.relu(-diff_klr).mean() # KLR must NOT decrease ) # Relation-entropy regularisation R = psi_model.get_relation_matrix() loss_rel_ent = -(R * torch.log(R+1e-8)).sum(1).mean() # → encourages sharp prototype assignments loss = (...base losses... + 0.02 * loss_rel_ent + 0.20 * loss_mono)

## Slide 7
Loss Function: M7 vs M8
M8 = M7 base losses + two new physics-informed terms
Loss Component
Description
M7
M8
L_distill
MSE vs M6 teacher output
✓
✓
L_seq
SmoothL1 vs target curves
✓
✓
5·L_initial
MSE on first step (×5 weight)
✓
✓
L_shape
SmoothL1 on consecutive Δ curves
✓
✓
0.02·L_rel_ent
Entropy of R → sharp assignments
—
✓ NEW
0.2·L_physics
Monotonic penalty KL↓ KR↓ KLR↑
—
✓ NEW
All 6 components are computed on full 21-step curves — the model targets curve shape, not individual slot values.

## Slide 8
Parameter Efficiency: M7 vs M8
M8 achieves 19.7% compression vs the M6 teacher while M7 only achieved 1.5%
M6 Teacher (Reference)
56,646
M7 Ψ-Model
55,770
M8 Ψ-Model
45,486
Compression M7 vs M6
1.5 %
PARAMETER COUNT — BAR CHART
56,646
M6 Teacher
56,646
M7 Student
55,770
M7 Ψ-Model
46,326
M8 Student
45,486
M8 Ψ-Model
−19.7 %
compression vs M6
vs only −1.5% in M7

## Slide 9
Performance Comparison: M7 vs M8
M8 maintains strong accuracy (~R²=0.988) with significantly fewer parameters
OVERALL METRICS (TEST SET — Ψ-Model only)
M6 Teacher R²
0.9804
M7 Ψ-Model R²
0.9897
M8 Ψ-Model R²
0.9882
M7 RMSE
21.60 B
M8 RMSE
23.06 B
M8 Curve MAPE
2.48 %
PER-VARIABLE PERFORMANCE — Ψ-MODEL
Variable
M7 R²
M8 R²
M7 RMSE
M8 RMSE
KL (lateral stiffness)
0.9910
0.9888
61.1 M
68.1 M
KR (rotational stiffness)
0.9807
0.9780
37.4 B
39.9 B
KLR (coupling)
0.9860
0.9845
1.29 B
1.36 B
STRUCTURE DISCOVERY (STAGE B)
M7 k*
6 prototypes
M7 Silhouette
0.7146
M8 k*
5 prototypes
M8 Silhouette
0.6490
Note: slight accuracy trade-off (-0.0015 R²) is the cost of 19.7% compression + physics guarantee.

## Slide 10
Summary: M7 → M8 Key Takeaways
Three targeted upgrades deliver compression, adaptability, and physical correctness
WHAT CHANGED FROM M7 TO M8
Feature
M7
M8
Slot MLP
64→128→64
64→48→64 ↓
Relation Matrix R
Fixed buffer
Learnable logits ✓
Physics loss
None
0.2 × L_mono
Entropy loss
None
0.02 × L_rel_ent
Student params
56,646
46,326 (−18.1%)
Ψ-Model params
55,770
45,486 (−18.4%)
Compression vs M6
1.5 %
19.7 % ✓✓
k* prototypes
6
5
Ψ-Model R² (test)
0.9897
0.9882 (~same)
CONCLUSIONS
M8 is a leaner, physics-aware version of M7
19.7% fewer parameters versus M6 teacher
Accuracy trade-off minimal: ΔR² = −0.0015
Learnable R enables better prototype assignment
Physics loss guarantees monotonic degradation
Curve MAPE = 2.48% confirms full-curve accuracy
M8 achieves the best balance between model size, accuracy, and physical interpretability in the Ψ-NN pipeline.