## Slide 1
M7 vs M8 vs M9
Master Technical Analysis with Full Architecture Drawings
M7 Baseline
Parameters: 55,770
R2: 0.9897
M8 Efficient
Parameters: 45,486
R2: 0.9882
M9 SwiGLU
Parameters: 45,502
R2: 0.9891
This deck explains model evolution, why M9 architecture matters, and how each design choice impacts accuracy, compression, and robustness.
PFE | M7-M8-M9 Master Analysis

## Slide 2
Executive Snapshot
What changed from M7 to M8 to M9
M7 Core
- Wide slot MLP: 64 -> 128 -> 64
- Fixed relation matrix
- k*=6 prototypes
- R2=0.9897
- Params=55,770
M8 Core
- Bottleneck MLP: 64 -> 48 -> 64
- Learnable relation matrix
- Physics monotonic loss
- k*=5 prototypes
- R2=0.9882
- Params=45,486
M9 Core
- SwiGLU gated MLP (hidden=32)
- Learnable relation matrix (same principle as M8)
- Full A/B/C retraining in latest run
- k*=5 prototypes
- R2=0.9891
- Params=45,502
PFE | M7-M8-M9 Master Analysis

## Slide 3
Problem and Outputs
Predict pile stiffness degradation across 21 steps
Input Features (8)
PI, Gmax, v, Dp, Tp, Lp, Ip, Dp/Lp
Model sees one scenario and predicts full time response.
Data:
- 1019 scenarios
- Train 815
- Test 204
Psi-NN Core
Slot attention
Per-slot MLP
Relation matrix R
Output head
Differences between M7/M8/M9 happen here.
Outputs (3 x 21)
KL: lateral stiffness
KR: rocking stiffness
KLR: coupling stiffness
Targets:
- High R2
- Low RMSE / MAE
- Physically consistent trends
PFE | M7-M8-M9 Master Analysis

## Slide 4
M7 Architecture (Drawn)
Baseline structured model
M7
Input (8)
Soil + pile features
Embedding 8->64
Feature lift
Slot Attention
1 initial + 6 prototype slots
Slot MLP
64->128->64 (GELU)
Fixed Relation Matrix
20x6, frozen
Output Head
64->3 then cumsum
Total 55,770
M7 Notes
- Strong baseline accuracy
- High MLP parameter cost
- Relation matrix cannot adapt after initialization
- Best in this snapshot by pure R2 but weak compression
PFE | M7-M8-M9 Master Analysis

## Slide 5
M8 Architecture (Drawn)
Efficiency upgrades + learnable structure
M8
Input (8)
Same data interface
Embedding 8->64
Same
Slot Attention
1 initial + 5 prototypes
Slot MLP
64->48->64 bottleneck
Learnable R
20x5 logits->softmax
Output + Physics
KL/KR down, KLR up
Total 45,486
M8 Upgrades
- MLP parameter drop by about 62% versus M7 MLP block
- Learnable relation matrix allows end-to-end adaptation
- Physics-aware loss improves physical plausibility
- Compression jumps to 19.7% vs M6
PFE | M7-M8-M9 Master Analysis

## Slide 6
M9 Architecture (Drawn)
SwiGLU gating replaces plain MLP
M9
Input (8)
Same
Embedding 8->64
Same
Slot Attention
1 initial + 5 prototypes
SwiGLU MLP
gate/value branches, hidden=32
Learnable R
20x5 logits->softmax
Output + Physics
same constraints
Total 45,502
M9 Intent
- Keep M8 compactness while increasing representational power
- SwiGLU gating selects informative channels per slot
- Maintains learnable relation matrix and physics constraints
- Strong KL and KLR improvements in latest full retrain
PFE | M7-M8-M9 Master Analysis

## Slide 7
Side-by-Side Architecture Map
Pipeline is shared, key differences highlighted
M7
Slot MLP
64->128->64
R matrix
fixed
k*
6 prototypes
R2 0.9897
M8
Slot MLP
64->48->64
R matrix
learnable
k*
5 prototypes
R2 0.9882
M9
Slot MLP
SwiGLU hidden=32
R matrix
learnable
k*
5 prototypes
R2 0.9891
PFE | M7-M8-M9 Master Analysis

## Slide 8
Learnable Relation Matrix (logits -> softmax)
From fixed mixing to trainable prototype routing
Definition
R_logits is a trainable tensor with shape (20, k*).
Each row corresponds to one reconstructed drop slot.
Conversion to valid weights
R_soft = softmax(R_logits, dim=1)
This ensures each row sums to 1.
Reconstruction
drop_slots = R_soft @ prototype_slots
Why this matters
- Gradients update routing weights
- Matrix can adapt to data and loss
- Better than frozen heuristic weights
Visual pipeline
prototype slots (k* vectors) -> R logits -> row softmax -> weighted sum -> 20 drop slots
In M7: R is fixed. In M8/M9: R is learned.
Observed in M9 full retrain
- k* = 5
- Learned R max-per-row average = 1.000
- Sparsity (<0.05 entries): 80/100
Interpretation: routing becomes highly selective.
PFE | M7-M8-M9 Master Analysis

## Slide 9
SwiGLU Gated MLP
How M9 increases expressiveness without large parameter growth
SwiGLU equation
gate = SiLU(W_gate x)
value = W_val x
out = W_out (gate * value)
Mechanism
- gate branch controls importance per dimension
- value branch carries content
- element-wise multiplication acts as dynamic filter
Result
More expressive than plain GELU MLP at similar size
x (64)
Gate path: SiLU(W_gate x)
Value path: W_val x
Element-wise gate * value
W_out -> output (64)
Parameter comparison of slot MLP block
M7 wide: 16,512
M8 bottleneck: 6,256
M9 SwiGLU: 6,272
PFE | M7-M8-M9 Master Analysis

## Slide 10
Parameter Comparison
Compression vs representation trade-off
Chart: 
| M6 | M7 | M8 | M9
Total params | 56646 | 55770 | 45486 | 45502
Model | Params | Compression vs M6 | MLP core
M7 | 55,770 | 1.5% | Wide MLP 64->128->64
M8 | 45,486 | 19.7% | Bottleneck MLP 64->48->64
M9 | 45,502 | 19.7% | SwiGLU gated MLP (hidden=32)
Interpretation
M8/M9 remove about 10.3k parameters versus M7.
M9 keeps M8-size efficiency while adding gating expressiveness.
PFE | M7-M8-M9 Master Analysis

## Slide 11
Accuracy and Error Rate
R2 higher is better, RMSE/MAE lower is better
Chart: 
| M7 | M8 | M9
R2 | 0.98966 | 0.98822 | 0.98908
Chart: 
| M7 | M8 | M9
RMSE (B) | 21.6004 | 23.0569 | 22.1948
Chart: 
| M7 | M8 | M9
MAE (B) | 3.1758 | 3.3142 | 3.3286
Model | R2 | RMSE | MAE | Error rate (1-R2)
M7 | 0.9897 | 2.160e+10 | 3.176e+09 | 0.0103
M8 | 0.9882 | 2.306e+10 | 3.314e+09 | 0.0118
M9 | 0.9891 | 2.219e+10 | 3.329e+09 | 0.0109
PFE | M7-M8-M9 Master Analysis

## Slide 12
Per-Variable Performance
KL, KR, KLR detailed view
Model | KL R2 | KR R2 | KLR R2 | KL RMSE | KR RMSE | KLR RMSE
M7 | 0.9910 | 0.9807 | 0.9860 | 6.106e+07 | 3.739e+10 | 1.292e+09
M8 | 0.9888 | 0.9780 | 0.9845 | 6.811e+07 | 3.991e+10 | 1.360e+09
M9 | 0.9905 | 0.9796 | 0.9860 | 6.259e+07 | 3.842e+10 | 1.290e+09
Key observations
- M9 has the best KL and KLR R2 among M7/M8/M9 in this run
- KR remains the hardest target and dominates RMSE scale
Error-rate takeaway
- Absolute R2 differences are small between M7 and M9
- M9 advantage is efficiency + architectural scalability
PFE | M7-M8-M9 Master Analysis

## Slide 13
Training Pipeline
M9 full retraining: Stage A -> Stage B -> Stage C
Stage A: Distillation
Train SwiGLU student from teacher
Early stopped at epoch 1118
Student R2: 0.9885
Stage B
Cluster slots
k*=5
Silhouette=0.673
Stage C: Structured M9
Train final Psi model
Early stopped at epoch 572
Final R2: 0.9891
Item | M7 | M8 | M9 (latest)
A/B/C pipeline | Yes | Yes | Yes
k* discovered | 6 | 5 | 5
Relation matrix | Fixed | Learnable | Learnable
MLP type | Wide GELU | Bottleneck GELU | SwiGLU gated
PFE | M7-M8-M9 Master Analysis

## Slide 14
M9 Robustness Analysis
Scenario-level diagnostics
Global quality
- Avg curve MAPE: 2.372%
- Median MAPE: 1.359%
- Avg curve R2: 0.98292
- P95 MAPE: 6.281%
- Test scenarios: 204
Worst-case signal
- Worst scenario id: 56
- Worst avg MAPE: 34.35%
- Worst avg R2: 0.1195
- Use uncertainty flag for extreme edge cases
Chart: 
| S56 | S141 | S73 | S84 | S60 | S137
MAPE % | 34.35 | 25.313 | 22.412 | 13.263 | 13.104 | 12.34
Interpretation
Most scenarios are very accurate.
A small tail of hard scenarios drives peak error.
This pattern is common in compact physics-informed models.
PFE | M7-M8-M9 Master Analysis

## Slide 15
Recommendation and Best-Model View
Decision using accuracy, compression, and architecture maturity
Criterion | M7 | M8 | M9
Overall R2 | 0.9897 | 0.9882 | 0.9891
Compression vs M6 | 1.5% | 19.7% | 19.7%
Learnable relation matrix | No | Yes | Yes
Gated MLP | No | No | Yes
Scalability for future tuning | Medium | High | Highest
Best practical choice
M9
Why:
- near-top accuracy
- major compression
- learnable routing
- SwiGLU expressiveness
- strongest foundation for next tuning round
Next tuning to beat current R2
- Increase Stage C patience and lower LR for finer convergence
- Run 3-5 seeds and keep best checkpoint
- Augment hard scenarios from the top error tail
PFE | M7-M8-M9 Master Analysis

## Slide 16
Closing Summary
M9 architecture value in one page
M7 -> M8 -> M9 evolution
M7 established the baseline structured Psi-NN.
M8 introduced compactness and learnable relation routing.
M9 adds SwiGLU gated slot MLP on top of that structure.
Learnable relation matrix (logits -> softmax)
lets the model learn prototype-to-time-step assignment end-to-end.
SwiGLU gated MLP
improves expressive filtering at almost identical parameter budget.
Current full-retrain M9: R2=0.9891, params=45,502.
This is a strong compact model and a solid base for final hyperparameter optimization.
PFE | M7-M8-M9 Master Analysis