## Slide 1
M9: SwiGLU Ψ-NN Architecture
Physics-Informed Digital Twin for Pile Stiffness Degradation
A comprehensive overview of the M9 model, its evolution from M7 & M8, technical concepts explained simply, and full performance comparison.
Ψ-NN Pipeline
SwiGLU
XAI

## Slide 2
01 Executive Summary
✦ We predict how offshore wind turbine pile foundations lose stiffness during typhoons.
✦ The AI model learns the physics of soil degradation (KL, KR, KLR decrease over cyclic loading).
✦ M9 is the latest version: it uses a SwiGLU gating mechanism inside the neural network.
✦ The model was compressed from 56,646 → 45,502 parameters (19.7% smaller) without losing accuracy.
✦ R² score = 0.989 — the model explains 98.9% of the variance in real test data.
✦ Three-stage pipeline: Distillation → Structure Discovery → Structured Retraining.
Parameters
45,502
19.7% fewer than M6 teacher
Overall R²
0.9891
Exceeds M6 teacher (0.9804)
Prototypes k*
5
Replaces 20 independent slots

## Slide 3
02 What Problem Are We Solving?
🌊 THE PROBLEM
Offshore wind turbines (OWT) are built on pile foundations in the seabed.
Typhoons cause cyclic loading → soil around the pile degrades.
This reduces the pile's stiffness (how well it resists movement).
Three types of stiffness change:
• KL — lateral (sideways) spring stiffness ↓
• KR — rotational (rocking) spring stiffness ↓
• KLR — cross-coupling stiffness (increases ↑)
If stiffness drops too much → resonance risk → structural failure!
🧠 OUR SOLUTION
Build an AI "Digital Twin" that predicts stiffness degradation.
Input: 8 soil/pile parameters (PI, Gmax, v, Dp, Tp, Lp, Ip, Dp/Lp).
Output: KL, KR, KLR values at 21 time steps during the storm.
The model enforces physics:
• KL and KR must decrease monotonically ↓
• KLR must increase monotonically ↑
Trained on real experimental data (44 loading cycles per scenario).
Engineers can simulate "what-if" scenarios instantly.

## Slide 4
03 Technical Glossary — Key Terms Explained Simply
Ψ-NN (Psi Neural Network)
A neural network that discovers its own structure. Instead of a fixed design, it learns which internal components (slots) are redundant and merges them into fewer "prototypes".
Slot Attention
A mechanism where the model has multiple "slots" (like memory boxes). Each slot learns to represent a different aspect of the degradation process. The model attends to the input data to fill each slot with relevant information.
Distillation
Training a smaller "student" model to mimic a larger "teacher" model. The student learns from the teacher's outputs, achieving similar accuracy with fewer parameters.
SwiGLU
Swish-Gated Linear Unit — a modern feed-forward block used in LLaMA and PaLM. It splits the input into two branches: a "gate" (decides what to keep) and a "value" (the actual content), then multiplies them together. More expressive than standard GELU at the same parameter count.
Relation Matrix R
A learned mapping that shows how each of the 20 degradation steps relates to the k* prototypes. Think of it as a recipe: each step is a weighted blend of the prototype ingredients.
R² (R-squared)
A score from 0 to 1 measuring how well predictions match reality. R²=0.98 means the model explains 98% of the variation in the data. Higher is better.

## Slide 5
04 The 3-Stage Ψ-NN Pipeline
All three models (M7, M8, M9) follow the same 3-stage pipeline. The difference lies in the internal MLP design and training losses.
STAGE A
Distillation
The large M6 "teacher" (56,646 params) is frozen.
A smaller "student" model learns to produce the same outputs.
L1 regularisation forces the student to use sparse slot patterns.
Loss = MSE(student, teacher) + 0.5·MSE(student, data) + μ·L1(slots)
→
STAGE B
Structure Discovery
Extract the student's learned slot vectors (20 slots × 64 dimensions).
Compute cosine similarity → see which slots are redundant.
K-Means clustering → find k* prototype groups (k*=5 for M8/M9).
Build relation matrix R: how each slot maps to prototypes.
→
STAGE C
Ψ-Model Retraining
Build a new model with only k* prototypes instead of 20 slots.
Initialise prototypes from discovered centroids.
Train with multi-objective loss:
Distill + Data + Initial·5 + Shape + Entropy + Physics

## Slide 6
05 M6 Teacher — The Foundation
SlotAttentionDegradation (M6)
• The teacher model — the starting point for all Ψ-NN models.
• Uses 21 learnable slots (1 initial + 20 degradation steps).
• Each slot is a 64-dimensional vector refined through 3 iterations of:
1. Cross-attention: slots query the input embedding
2. Self-attention: slots communicate with each other
3. Feed-forward MLP: non-linear transformation (64→128→64, GELU)
• Physics constraint: KL, KR forced to decrease, KLR to increase via cumulative sums.
• Parameters: 56,646 | R² = 0.9804 | Trained on real OWT pile data.
⚠ Problem: 20 independent drop slots are redundant!
→ Many slots learn nearly identical representations (cosine sim > 0.99).
→ This motivates the Ψ-NN compression pipeline (M7, M8, M9).

## Slide 7
06 M7 — Baseline Ψ-NN
Architecture
• First implementation of the 3-stage Ψ-NN pipeline.
• Stage A: Student uses SAME architecture as M6 teacher (wide MLP 64→128→64).
• Stage B: K-Means finds k*=6 prototypes.
• Stage C: Ψ-Model uses FIXED relation matrix R (registered buffer, not learnable).
• Slot MLP: standard GELU MLP (64→128→64).
→ 2× expansion = many parameters.
• Stage C Loss: Distill + Data + Initial·5 + Shape.
→ No physics-monotonic penalty.
→ No relation-entropy regularisation.
Results & Limitations
Parameters: 55,770
Prototypes: k* = 6
Compression: only 1.5% fewer than M6
Overall R² = 0.9897
KL R² = 0.9910
KR R² = 0.9807
KLR R² = 0.9860
⚠ Limitations:
• Minimal compression (1.5%) — wide MLP wastes params.
• Fixed R matrix — cannot adapt during training.
• No physics loss — model may violate monotonicity.
• k*=6 prototypes — more than necessary.

## Slide 8
07 M8 — Efficient Ψ-NN (3 Upgrades)
Upgrade 1: EfficientSlotMLP
Replaces wide MLP (64→128→64) with bottleneck MLP (64→48→64).
• Input (64) → compress to 48 → GELU activate → expand back to 64.
• Saves ~40% of MLP parameters.
• GELU non-linearity preserves expressiveness.
• 6,256 params vs M6's 16,576 MLP params.
Upgrade 2: Learnable R Matrix
Relation matrix R is no longer frozen!
• Stored as learnable logits: R = softmax(logits).
• Row-normalised → each slot gets valid mixing weights.
• Initialised from Stage B clustering, then fine-tuned end-to-end.
• + Entropy regularisation: sharpens assignments (avoids uniform mixing).
Upgrade 3: Physics-Monotonic Loss
A new penalty term enforces physical laws during training.
• Penalises any KL or KR that INCREASES between time steps.
• Penalises any KLR that DECREASES between time steps.
• L_mono = relu(ΔKL, ΔKR) + relu(-ΔKLR)
• Weighted by λ=0.2 in total loss.
M8 Result: 45,486 params | k*=5 | 19.7% compression | R²=0.9882 | Learnable R ✓ | Physics loss ✓

## Slide 9
08 M9 — SwiGLU Ψ-NN (The Latest)
The SwiGLU Upgrade
M9 replaces the EfficientSlotMLP (M8) with a SwiGLU feed-forward block.
How SwiGLU works (3 linear projections):
1. W_gate(x) → apply SiLU activation → produces the "gate" signal
2. W_val(x) → raw projection → produces the "value" signal
3. gate ⊙ value (element-wise multiply) → gated output
4. W_out(gated) → project back to original dimension
Why SwiGLU is better:
• The gate learns WHICH features to propagate (selective filtering)
• Used in state-of-the-art LLMs: LLaMA, PaLM, Mistral
• Same parameter count as M8 bottleneck (6,272 ≈ 6,256)
• But provably more expressive due to multiplicative gating
M9 keeps ALL M8 improvements:
✓ Learnable relation matrix (softmax logits)
✓ Physics-monotonic loss + entropy regularisation
✓ Same training pipeline (A → B → C)
M9 Quick Stats
Parameters
45,502
Compression
19.7%
k* prototypes
5
SwiGLU hidden
32
Overall R²
0.9891
KL R²
0.9905
KR R²
0.9796
KLR R²
0.9860

## Slide 10
09 SwiGLU vs GELU MLP — Schematic Comparison
M7: Standard GELU MLP
64 → 128 → 64 (16,576 params)
Input x ∈ ℝ⁶⁴
↓
W₁ · x + b₁
Linear 64→128
↓
GELU(·)
Activation
↓
Dropout(0.1)
Regularisation
↓
W₂ · h + b₂
Linear 128→64
↓
Output ∈ ℝ⁶⁴
M8: Bottleneck MLP
64 → 48 → 64 (6,256 params)
Input x ∈ ℝ⁶⁴
↓
W₁ · x + b₁
Linear 64→48
↓
GELU(·)
Activation
↓
Dropout(0.1)
Regularisation
↓
W₂ · h + b₂
Linear 48→64
↓
Output ∈ ℝ⁶⁴
M9: SwiGLU MLP
Gate + Value parallel (6,272 params)
Input x ∈ ℝ⁶⁴
↙
↘
W_gate·x
↓
SiLU(·)
W_val·x
↘
↓
gate ⊙ value
↓
Dropout(0.1)
↓
W_out → ℝ⁶⁴
Output ∈ ℝ⁶⁴

## Slide 11
10 M9 + Cross-Attention Adapter (Stage D)
An optional decoder-style extension inspired by the SCm→WTm encoder-decoder coupling in the research paper.
Adapter Architecture (Schematic)
Input x → M9 Encoder (FROZEN)
↓
Frozen Slot States S_f ∈ ℝ²¹ˣ⁶⁴
↓
Learned Decoder Queries Q
↓
Cross-Attn(Q, K=S_f, V=S_f)
↓
LayerNorm(Q + Attn_out)
↓
σ(gate) · decoded + S_f
↓
Output Heads → Final Prediction
How It Works
1. The entire M9 base model is FROZEN (no gradients).
2. A new set of learnable "decoder queries" is created.
3. These queries attend to the frozen M9 slot states via cross-attention.
4. A learnable gate (sigmoid) controls how much adapter output is mixed in.
5. Only the adapter's parameters are trained (~18,241 trainable).
Key Metrics:
Total params: 63,743
Trainable params: 18,241 (adapter only)
Base R²: 0.9891 (frozen M9)
Adapter R²: 0.9881
💡 The adapter allows extending M9 without modifying the base model —
useful for domain adaptation or multi-task scenarios.

## Slide 12
11 M7 vs M8 vs M9 — Comparison Table
Feature
M7 (Baseline)
M8 (Efficient)
M9 (SwiGLU)
Slot MLP Type
GELU 64→128→64
Bottleneck 64→48→64
SwiGLU (gate+val, h=32)
MLP Parameters
16,576
6,256
6,272
Total Params
55,770
45,486
45,502
Compression vs M6
1.5%
19.7%
19.7%
k* (Prototypes)
6
5
5
Relation Matrix R
Fixed (frozen buffer)
Learnable (softmax)
Learnable (softmax)
Physics-Mono Loss
✗ No
✓ Yes (λ=0.2)
✓ Yes (λ=0.2)
Entropy Regularise
✗ No
✓ Yes (λ=0.02)
✓ Yes (λ=0.02)
Overall R²
0.9897
0.9882
0.9891
KL R²
0.9910
0.9888
0.9905
KR R²
0.9807
0.9780
0.9796
KLR R²
0.9860
0.9845
0.9860
Cross-Attn Adapter
✗ No
✗ No
✓ Optional (Stage D)

## Slide 13
12 Performance Metrics — Visual Summary
Overall R² Score (higher = better)
M6 Teacher
56,646 params
0.9804
M7 Ψ-NN
55,770 params
0.9897
M8 Efficient
45,486 params
0.9882
M9 SwiGLU
45,502 params
0.9891
Per-Variable R² Comparison
KL (Lateral Stiffness)
M6
0.9768
M7
0.9910
M8
0.9888
M9
0.9905
KR (Rotational Stiffness)
M6
0.9634
M7
0.9807
M8
0.9780
M9
0.9796
KLR (Cross-Coupling)
M6
0.9690
M7
0.9860
M8
0.9845
M9
0.9860

## Slide 14
13 Key Takeaways
🏗️ M7 → Proof of concept
Demonstrated Ψ-NN compression works: 21 slots → 6 prototypes. But minimal compression (1.5%) and no physics enforcement in Stage C.
⚡ M8 → Efficiency + Physics
Bottleneck MLP cuts parameters by 19.7%. Learnable R matrix adapts during training. Physics-monotonic loss ensures KL↓, KR↓, KLR↑.
🧬 M9 → SwiGLU gating
Replaces bottleneck with SwiGLU: same param count but better expressiveness thanks to multiplicative gating. Best R² of all compressed models (0.9891).
🔌 Cross-Attention Adapter
Optional Stage D: freeze M9, train only a decoder-style adapter. Enables domain adaptation without touching the base model.
📊 Bottom Line
M9 achieves 98.91% variance explained with 19.7% fewer parameters than the original teacher. Physics constraints are built into both the architecture (cumsum) and the loss function.

## Slide 15
Thank You
M9: SwiGLU Ψ-NN for Pile Stiffness Degradation
Physics-informed · Compressed · Explainable · Extensible