## Slide 1
M9 → M10 : Explainable AI (XAI) Enhancement
From Black-Box SwiGLU Ψ-NN to Interpretable Stiffness Predictions
Three New XAI Capabilities in M10
▸ Layer-wise Relevance Propagation (LRP)
Gradient × Input attribution → 8 raw input features × 21 steps × 3 variables
▸ Attention Rollout — Cross & Self separated
Cross: input→slot information flow | Self: slot→slot flow with residual mixing
▸ Integrated Gradients
Path-based attribution satisfying the completeness axiom f(x)−f(0) = Σⱼ attrⱼ
Same base model weights • No retraining required • XAI computed on demand per scenario
Physics-Informed Digital Twin — SwiGLU Slot-Attention ΨNN — Pile Stiffness Degradation

## Slide 2
M9 Baseline Architecture (Unchanged in M10)
SwiGLU Ψ-NN • 3-Stage Pipeline • 56,646 → ~30,000 params via distillation
Stage A
Distillation
• M6 Teacher (56,646 params, frozen)
• Student mimics teacher + data
• SwiGLU MLP replaces GELU MLP
• L1 regularisation on slots
• Loss: L_distill + 0.5·L_data + μ·L1
Stage B
Structure Discovery
• Extract student slot vectors [20, 64]
• KMeans clustering (k=2..10)
• Silhouette score → k* = 5
• Compute relation matrix R [20 × k*]
• Centroids initialise Ψ-model prototypes
Stage C
SwiGLU Ψ-Model Training
• k* prototype slots + learnable R
• drop_slots = softmax(R) × prototypes × scale
• Same attention core as M6/M9
• Multi-objective: distill + seq + shape
• + physics monotonicity + relation entropy
Core Iterative Block (×3 iterations)
Cross-Attention
Q=slots[21,64] K,V=x_embed[1,64] 4 heads, batch_first
Self-Attention
Q,K,V=slots[21,64] 4 heads slot↔slot mixing
SwiGLU MLP
gate = SiLU(W_gate·x) val = W_val·x out = W_out(gate⊙val)
Prediction Heads
initial_proj: 64→32→3 drop_proj: 64→32→3 cumsum for curves

## Slide 3
M10: What Changed? (Architecture Diff)
✓ UNCHANGED (M9 → M10)
SlotAttentionPsiModel class — identical architecture
SwiGLUSlotMLP(d=64, hidden=32) — same gating
3-stage pipeline: distill → cluster → Ψ-train
Multi-head attention: 4 heads, d_model=64
3 refinement iterations per forward pass
Physics constraints: KL↓, KR↓, KLR↑ monotonicity
Relation matrix R with softmax normalisation
k*=5 prototype slots from silhouette analysis
Prediction: initial + cumsum(constrained drops)
Model weights: pile_model.pth (no retraining)
★ NEW in M10
▸ xai_engine.py (280 lines)
New module — 3 XAI methods + orchestrator
▸ forward_with_attention()
Modified forward pass returning attention matrices
▸ Gradient × Input LRP
attribution[3, 21, 8] → 8 raw features
▸ Integrated Gradients
Path integral for exact completeness axiom
▸ Cross-Attention Rollout
Per-iteration [B,21,1] → averaged & normalised
▸ Self-Attention Rollout
Residual mixing: (1−w)·I + w·A, then multiplicative
▸ Curve-based R² / MAPE
Per-scenario per-variable → averaged (not flattened)
▸ /xai dashboard + /api/xai
Full interactive web page with heatmaps
▸ R² consistency fix
Override comparison & analysis with live-computed values
MODEL PARAMS
Same ≈30K
NEW CODE
+280 lines
RETRAINING
None
NEW ROUTES
/xai + API

## Slide 4
XAI Method 1: Layer-wise Relevance Propagation (LRP)
Gradient × Input — propagates relevance back to 8 raw input features
Algorithm (compute_gradient_x_input)
For each variable v ∈ {KL, KR, KLR}:
For each step s ∈ {1, ..., 21}:
x_input ← x.clone().requires_grad_(True)
output = model(x_input, seq_len=21)
target = output[0, s, v]
target.backward()
grad = x_input.grad → shape [8]
attribution[v, s] = grad × x → [8]
Result: attribution[3, 21, 8]
= 3 variables × 21 steps × 8 features
Mathematical Foundation
Completeness (1st-order Taylor):
f(x) ≈ f(0) + Σⱼ xⱼ · ∂f/∂xⱼ
Attribution for feature j:
Rⱼ = xⱼ × ∂ŷ(v,s) / ∂xⱼ
8 Raw Input Features
PI — Plasticity Index
Gmax — Max Shear Modulus (Pa)
ν — Poisson's Ratio
Dp — Pile Diameter (m)
Tp — Pile Wall Thickness (m)
Lp — Pile Length (m)
Ip — Moment of Inertia
Dp/Lp — Slenderness Ratio
Output: Feature Attribution Heatmap
attribution[v, s, f] = relevance of feature f at step s for variable v
S1 S2 S3 ... S21
PI
Gmax
ν
Dp
Tp
Lp
Ip
Dp/Lp
Interpretation:
▸ Red cells: feature pushes prediction UP
▸ Blue cells: feature pushes prediction DOWN
▸ Intensity ∝ |attribution| (abs relevance)
▸ Rows sum → feature importance ranking:
imp(f) = Σₛ |attribution[v,s,f]| / total × 100%
▸ KL variable: Dp/Lp dominates at ~73%
▸ Gmax is 2nd most influential (~14%)

## Slide 5
XAI Method 2: Attention Rollout (Cross + Self, Separately)
Traces information flow through the 3-iteration slot attention mechanism
Cross-Attention Rollout
How much does each slot pull from the input?
For iteration l ∈ {1, 2, 3}:
cross_attn(Q=slots, K=x_embed, V=x_embed)
→ weights_l [B, 21, 1] (21 queries, 1 key)
Squeeze → per_iter_l [B, 21]
Rollout = mean(per_iter_1, per_iter_2, per_iter_3)
Normalise: rollout /= rollout.sum() → [B, 21]
Output: one scalar per slot (0..1)
= fraction of input info flowing to that slot
Slot 1 (initial) vs Slots 2-21 (drops)
Self-Attention Rollout
How do slots exchange information with each other?
For iteration l ∈ {1, 2, 3}:
self_attn(Q=slots, K=slots, V=slots)
→ weights_l [B, 21, 21] (full slot×slot)
Residual mixing (w = 0.5):
A'_l = (1−w)·I + w·A_l ← 50% identity
Re-normalise rows to sum to 1
Multiplicative rollout:
R = A'_3 × A'_2 × A'_1 ← matrix multiply
→ [B, 21, 21] aggregated slot-to-slot flow
Why Separate Cross and Self Attention?
Cross-attention answers:
Which input features does each slot care about?
input → slot flow — one source token (the 8-feature embedding), 21 query slots
Self-attention answers:
Which degradation steps influence each other?
slot → slot flow — 21×21 attention matrix per iteration, captures temporal dependencies
Combined insight:
Cross = feature sensitivity per slot + Self = temporal coupling between steps
Together they explain WHY the model predicts a particular degradation trajectory shape

## Slide 6
XAI Method 3: Integrated Gradients (Gold Standard)
Path-based attribution — exact completeness axiom (Sundararajan et al., ICML 2017)
Mathematical Definition
Completeness Axiom:
f(x) − f(baseline) = Σⱼ attributionⱼ
Attribution for feature j:
IGⱼ = (xⱼ − baseⱼ) × ∫₀¹ ∂f/∂xⱼ(base + α(x−base)) dα
Numerical approximation (M = 30 steps):
IGⱼ ≈ (xⱼ − 0) × (1/M) Σₘ ∂f/∂xⱼ(αₘ · x)
where αₘ = (m + 0.5) / M
Algorithm (compute_integrated_gradients)
baseline = zeros_like(x) ← zero baseline
For each variable v, step s:
total_grad = 0
For m = 0..29: (30 integration steps)
α = (m + 0.5) / 30
x_interp = α · x
output = model(x_interp)
target = output[0, s, v]
target.backward()
total_grad += x_interp.grad
attr[v,s] = x × total_grad / 30
Comparison: Gradient×Input vs Integrated Gradients
Property
Gradient × Input (Method 1)
Integrated Gradients (Method 3)
Completeness
≈ 1st order Taylor approx
Exact (sum = f(x) − f(0))
Speed
~50 ms per scenario
~2 s per scenario (30× slower)
Gradient calls
3 × 21 = 63
3 × 21 × 30 = 1,890
Sensitivity
High (local gradient)
High (path-averaged)
Saturation robust
No (can miss saturated features)
Yes (integrates full path)
Implementation
compute_gradient_x_input()
compute_integrated_gradients()
Default usage
✓ Used in /api/xai (fast)
Available via method='ig'

## Slide 7
M10 XAI Data Flow: From Input to Explanation
Input
x ∈ ℝ⁸
Input Embed
Linear(8→64)
LayerNorm
GELU
Cross-Attn
Q=slots K,V=embed
→ weights [21,1]
Self-Attn
Q,K,V = slots
→ weights [21,21]
SwiGLU MLP
SiLU(W_g·x)⊙W_v·x
→ residual
Prediction
initial + cumsum
→ [21, 3]
Output
KL, KR, KLR
21 steps
× 3 iterations
XAI Extraction Layer (M10 NEW)
Cross-Attn
Rollout
avg 3 iters → [21]
normalise sum=1
Self-Attn
Rollout
(1−w)I + wA per iter
multiply → [21×21]
Gradient × Input
(LRP)
∂ŷ/∂x × x
→ [3, 21, 8]
Integrated
Gradients
∫₀¹ ∂f/∂x dα × x
→ [3, 21, 8]
Feature
Importance
Σₛ|attr[v,s,f]|/total
→ % per feature

## Slide 8
M10 Fix: Curve-Based Error Metrics (R² Consistency)
✗ M9 Problem: R² Discrepancy
Main page banner: R² = 0.9847
Diagnosis page: R² = 0.9829
Difference: 0.0018 (not just rounding!)
Root causes:
1. JS re-averaged already-rounded values
→ scenarios.reduce(avg_r2) → double rounding
2. Different data sources:
Main: computed at runtime from model
Diag: read from scenario_analysis.json
(pre-computed, possibly stale)
✓ M10 Solution
All errors computed on cumulative curves:
For each scenario i, variable v:
R²(i,v) = 1 − SS_res/SS_tot
MAPE(i,v) = mean(|t−p|/|t|) × 100
Curve R² = mean over all (i, v)
Single source of truth (Python-computed):
metrics_cache['overall']['curve_r2']
Overrides applied at load time:
comparison_data → uses curve R²
scenario_analysis → uses curve R²
Before (M9):
Main R²=0.9847 ≠ Diagnosis R²=0.9829 (two different computations)
After (M10):
Main R²=0.9847 = Diagnosis R²=0.9847 (same Python value, overridden)
M10 Metric Definitions (Standardised)
Curve MAPE
Mean Abs % Error computed on the 21-step KL/KR/KLR curves, per scenario, then averaged
Curve R²
Per-scenario per-variable R², then averaged across all scenarios and variables
Curve NRMSE
RMSE / range(target) × 100%, per variable per scenario, then averaged

## Slide 9
M10 Interactive XAI Dashboard (/xai)
Full interactive web page — per-scenario explainability computed on demand
Feature Attribution Heatmap
▸ 8 features × 21 steps colour grid
▸ Red = positive, Blue = negative relevance
▸ Tab-switchable: KL / KR / KLR
▸ Feature importance bar chart (sorted %)
▸ Hover tooltip: exact attribution value
Cross-Attention Analysis
▸ 3 bar charts (one per iteration)
▸ Rollout chart (averaged + normalised)
▸ Shows input→slot information flow
▸ 21 bars = one per degradation slot
▸ Height ∝ how much slot queries input
Self-Attention Heatmap
▸ 3 iteration heatmaps (21 × 21 each)
▸ Rollout heatmap (multiplicative)
▸ 50% residual mixing per iteration
▸ Row = query, Column = key
▸ Purple intensity ∝ attention weight
API Endpoint: /api/xai/<scenario_idx>
Request: GET /api/xai/0 (scenario index 0-203)
Computation: XAIAnalyzer(model, feature_names).analyze(x_scaled[idx])
Response JSON keys:
cross_attention_rollout: [21] • cross_attention_per_iter: [3][21]
self_attention_rollout: [21][21] • self_attention_per_iter: [3][21][21]
lrp_attribution: {KL: [21][8], KR: [21][8], KLR: [21][8]}
feature_importance: {KL: [8], KR: [8], KLR: [8], combined: [8]}
Tech stack: Flask + Chart.js 4.4.7 • CSS Grid heatmaps (no Canvas for perf) • Zero new dependencies • ~50ms per gradient call • 200ms total XAI (incl. 3×21 backward passes)

## Slide 10
M10 File Structure & Summary
M10/ Directory
xai_engine.py
[NEW]
280 lines — 3 XAI methods + XAIAnalyzer orchestrator
train.py
[MODIFIED]
Curve-based metrics added, M10 headers
webapp.py
[MODIFIED]
XAI dashboard, R² fix, /xai route, /api/xai
run_app.bat
[MODIFIED]
Updated banner + XAI URL
pile_model.pth
[UNCHANGED]
SwiGLU Ψ-model weights (from M9 training)
psi_config.pkl
[UNCHANGED]
k*, relation matrix, scalers
psi_discovery.json
[UNCHANGED]
Clustering results, silhouettes
comparison.json
[MODIFIED]
R² now uses curve-based values
scenario_analysis.json
[UNCHANGED]
Pre-computed (overridden at runtime)
analyze_scenarios.py
[UNCHANGED]
GBR feature importance (M9)
M9 vs M10 Summary
Base Model
SwiGLU Ψ-NN
SwiGLU Ψ-NN (same)
Parameters
~30,000
~30,000 (unchanged)
Training
3-stage pipeline
No retraining needed
XAI Methods
None (black-box)
LRP + Attn Rollout + IG
Feature Attrib.
GBR only (external)
Gradient-based (internal)
Attn. Visibility
None
Cross + Self separately
Dashboard
Main + Diagnosis
Main + Diagnosis + XAI
R² Metric
Flattened (inconsistent)
Curve-based (consistent)
R² Source
JS recomputed
Python single source
API Routes
/ , /diagnosis
/ , /diagnosis , /xai
New Code
—
+280 lines (xai_engine)
Dependencies
torch, flask, sklearn
Same (zero new deps)
M9
M10
Key takeaway: M10 adds a complete Explainable AI layer to the existing M9 model without modifying model weights, without retraining, and without adding any external dependencies. The XAI engine runs on-demand per scenario, providing per-input-feature attribution across all 21 degradation steps and 3 stiffness variables.