## Slide 1
Research Internship Presentation
Physics-Informed AI Digital Twin for Offshore Wind Turbine Pile Foundation Stiffness Degradation Prediction
Internship at Zhejiang University (浙江大学), Hangzhou, China
KHALIL Youssef
PhD Student — Moroccan University ↔ Zhejiang University Collaboration
Supervisor Meeting — April 2026

## Slide 2
Agenda
01
Host Institution & Acceptance
02
PhD Program & Collaboration Framework
03
Research Subject: Why This Matters
04
Engineering Problem: OWT Pile Degradation
05
AI Approach: Physics-Informed Digital Twin
06
Model Architecture & Evolution (M5 → M9)
07
Key Innovation: SwiGLU Ψ-NN Pipeline
08
Results, Validation & Web Application
09
Research Contributions & Timeline
10
Conclusion & Next Steps
2/22

## Slide 3
Host Institution — Zhejiang University (浙江大学)
🏛 About Zhejiang University
• Founded: 1897 — one of China's oldest and most prestigious universities
• Location: Hangzhou, Zhejiang Province, China
• World Ranking: Top 50 globally (QS/THE rankings)
• Known as one of China's "C9 League" universities
(equivalent to the Ivy League in the US)
• Renowned for Engineering, Computer Science, and Civil Engineering
• Over 60,000 students, 5,700+ faculty members
• Strong research output with international collaborations
• The College of Civil Engineering and Architecture
hosts leading researchers in offshore geotechnical engineering
and AI-driven structural health monitoring
🔬 Research Laboratory
• Department: College of Civil Engineering & Architecture
• Research Focus:
— Offshore wind turbine (OWT) foundation engineering
— Soil-structure interaction under cyclic loading
— AI / Machine Learning for structural health monitoring
— Physics-informed neural networks
— Digital Twin technology for infrastructure
• Experimental Facilities:
— Advanced soil testing lab (cyclic loading apparatus)
— High-performance computing cluster for AI training
— Wind tunnel and wave flume testing facilities
• Active international PhD programs (CSC, bilateral)
3/22

## Slide 4
Acceptance Letter (邀请函) & PhD Admission
📄 Invitation/Acceptance Letter
• Official invitation letter (邀请函) received from
Zhejiang University, College of Civil Engineering
• The letter confirms:
✓ Acceptance as a visiting researcher / PhD student
✓ Access to research facilities and computing resources
✓ Supervision by faculty in offshore engineering group
✓ Research topic: AI-driven prediction of pile foundation
stiffness degradation under typhoon conditions
• Duration: Full academic year research period
• Status: Officially accepted and confirmed
• File reference: 邀请函 (1).pdf
🎓 PhD Program — Next Academic Year
• PhD admission document received and processed
(Reference: 20260417160802100_17 (1).pdf)
• Program: Doctoral research in Civil/Structural Engineering
with specialisation in AI for Infrastructure
• Framework: Joint supervision between
— Moroccan university (home institution)
— Zhejiang University (host institution)
• Research will continue for the next academic year
building upon the work initiated during the internship
• Expected outcomes:
— Published research papers (international journals)
— PhD thesis contribution
— Developed codebase & web application
4/22

## Slide 5
Supervision & Collaboration Framework
Joint Supervision Model
• This research internship operates under a bilateral collaboration between Morocco and China.
• The student (KHALIL Youssef) conducts research at Zhejiang University under Chinese supervision,
while maintaining academic reporting to the Moroccan university supervisor.
• Research findings, codebase, and publications are shared between both institutions.
• The project aligns with NSFC (National Natural Science Foundation of China) funded research
on typhoon-resistant design of offshore wind turbine foundations (面上项目 — General Program).
🇲🇦 Morocco — Home Institution
• University: Moroccan University (Home)
• Role: Academic framework & thesis committee
• Responsibilities:
— Validate research direction
— Thesis evaluation & defense
— Academic administration
🇨🇳 China — Host Institution
• University: Zhejiang University (浙江大学)
• Role: Research execution & lab access
• Responsibilities:
— Daily research supervision
— Access to data, computing, labs
— Research paper co-authorship
5/22

## Slide 6
Research Topic — Why This Matters
Predicting pile foundation stiffness degradation under typhoon-induced cyclic loading using physics-informed AI
🌍 Global Context
• Offshore wind energy is expanding rapidly worldwide.
• China plans 100+ GW of offshore wind by 2030.
• Morocco is developing its own offshore wind capacity.
• Most turbines use monopile foundations (5m diameter).
• Typhoons and storms create extreme cyclic loading.
• Foundation integrity is critical for safety & cost.
⚡ The Challenge
• When typhoons hit, soil around the pile degrades.
• Stiffness (how well the pile resists displacement) drops.
• If stiffness drops too much → resonance → failure.
• Current methods: expensive physical tests or slow FEM.
• No fast, accurate tool exists for real-time prediction.
• Engineers need a "what-if" simulator for design.
🧠 Our Solution
• Build an AI "Digital Twin" of the pile-soil system.
• The AI learns from real experimental data.
• It encodes fundamental physics laws into the network.
• Predictions are instantaneous (milliseconds vs hours).
• Engineers can test thousands of scenarios quickly.
• The model is explainable — not a black box.
6/22

## Slide 7
Engineering Problem: Pile Stiffness Degradation
What Happens During a Typhoon?
1. Wind & waves create cyclic lateral forces on the offshore wind turbine structure.
2. These forces are transferred through the tower to the monopile foundation in the seabed.
3. The surrounding soil is repeatedly loaded and unloaded → the soil progressively weakens.
4. This weakening is measured as three stiffness parameters that change over time:
KL — Lateral Stiffness
Resistance to sideways movement
↓ Decreases
KL < 0 drops (soil gets weaker laterally)
Hard-coded in the AI model (impossible to violate)
KR — Rotational Stiffness
Resistance to rocking/tilting
↓ Decreases
KR < 0 drops (soil resists less against tilting)
Hard-coded in the AI model (impossible to violate)
KLR — Cross-Coupling
Interaction between lateral & rotational
↑ Increases (→0)
KLR is negative, it increases toward zero
Hard-coded in the AI model (impossible to violate)
7/22

## Slide 8
Data & Physical Input Parameters
8 Input Features (Soil & Pile Properties)
PI
Plasticity Index
Soil classification (how "clayey" the soil is)
Gmax
Maximum Shear Modulus
Initial stiffness of the soil (Pa)
ν
Poisson's Ratio
Ratio of lateral to axial strain
Dp
Pile Diameter
Diameter of the monopile (m)
Tp
Pile Wall Thickness
Thickness of the pile wall (m)
Lp
Pile Embedded Length
Length of pile inside the seabed (m)
Ip
Moment of Inertia
Pile cross-section's resistance to bending
Dp/Lp
Diameter-to-Length Ratio
Aspect ratio of the pile
Dataset Summary
Total Scenarios
1,019
Training Set
815 (80%)
Test Set
204 (20%)
Time Steps
21 per scenario
Output Variables
3 (KL, KR, KLR)
Output Shape
[B, 21, 3]
Data: Real experimental data from cyclic loading tests on monopiles (REAL DATA.xlsx — 44 cycles per scenario, subsampled to 21 representative steps)
8/22

## Slide 9
AI Approach — Physics-Informed Digital Twin
Core Concept: Combine AI Power with Engineering Knowledge
Unlike pure black-box AI, our model embeds fundamental physics laws directly into the neural network architecture.
The model CANNOT violate these laws — they are structural constraints, not just penalties in the loss function.
🧠 Slot Attention Transformer
• 21 learnable memory "slots"
• Cross-attention to input data
• Self-attention between slots
• Iterative refinement (3 rounds)
• Each slot specializes in one
• degradation time step
⚙️ Physics Constraints
• KL, KR drops forced ≤ 0
• KLR drops forced ≥ 0
• Cumulative sum ensures
• monotonic trajectories
• Signed-log scaling preserves
• sign information (KLR < 0)
🔬 Ψ-NN Structure Discovery
• 20 slots → k* prototypes
• K-Means clustering on slots
• Relation matrix R maps
• steps to prototypes
• 19.7% parameter reduction
• Improved interpretability
9/22

## Slide 10
Model Architecture — Slot Attention Transformer
INPUT
8 features: PI, Gmax, ν, Dp, Tp, Lp, Ip, Dp/Lp
[B, 8]
EMBEDDING
Linear(8→64) + LayerNorm + GELU
[B, 1, 64]
21 LEARNABLE SLOTS
Slot 1 (initial) + Slots 2-21 (degradation)
[B, 21, 64]
ITERATIVE REFINEMENT ×3
Cross-Attn → Self-Attn → SwiGLU MLP
[B, 21, 64]
SLOT SPLIT
Slot 1 → Initial Head | Slots 2-21 → Drop Head
Split
PHYSICS CONSTRAINTS
ΔKL,ΔKR = -|d| | ΔKLR = +|d|
Hard-coded
CUMULATIVE SUM
K(t) = K⁰ + Σ constrained drops
[B, 21, 3]
OUTPUT
KL(t), KR(t), KLR(t) for t=1...21
[B, 21, 3]
10/22

## Slide 11
Model Evolution: M5 → M6 → M7 → M8 → M9
M5
LSTM + Slot Attn
Baseline with LSTM decoder
157,958
params
R²=0.9913
LSTM decoder for sequential drops | 2 refinement iterations | KLR unconstrained
M6
Simplified Teacher
Remove LSTM, add KLR constraint
56,646
params
R²=0.9804
Remove LSTM (64% fewer params) | 3 refinement iterations | All 3 stiffnesses constrained
M7
Baseline Ψ-NN
First compression attempt
55,770
params
R²=0.9897
3-stage pipeline (first attempt) | Fixed relation matrix R | k*=6 prototypes, wide MLP
M8
Efficient Ψ-NN
Bottleneck MLP + Learnable R
45,486
params
R²=0.9882
Bottleneck MLP (64→48→64) | Learnable R (softmax logits) | Physics-monotonic loss
M9
SwiGLU Ψ-NN ★
Best: SwiGLU gating mechanism
45,502
params
R²=0.9891
SwiGLU feed-forward (gate×value) | Same param count as M8 | Higher R² from better gating
11/22

## Slide 12
M9: SwiGLU Ψ-NN — The Current State of the Art
What is SwiGLU? (The Key Innovation)
SwiGLU = Swish-Gated Linear Unit
Used in state-of-the-art AI: LLaMA, PaLM, Mistral
How it works (inside each slot's feed-forward block):
Input x (64-dim vector)
↓ ↓
W_gate · x W_val · x
↓ ↓
SiLU(·) (raw value)
↓ ↓
gate × value ← element-wise multiply
↓
W_out · (gated) → Output (64-dim)
Why it's better:
• The gate learns WHICH features to propagate
• More expressive than simple GELU at same param count
• 6,272 params (≈ same as M8's 6,256)
• But achieves higher R² (0.9891 vs 0.9882)
M9 Performance Summary
Parameters
45,502
Compression vs M6
19.7% fewer
Prototypes k*
5
SwiGLU hidden dim
32
Overall R²
0.9891
KL R²
0.9905
KR R²
0.9796
KLR R²
0.9860
Curve MAPE
2.37%
Curve R²
0.9829
Test Scenarios
204
12/22

## Slide 13
3-Stage Ψ-NN Training Pipeline
STAGE A
Distillation
• M6 teacher (56,646 params) is frozen
• Student learns to mimic teacher output
• SwiGLU MLP in student (M9 upgrade)
• L1 regularisation → sparse slot patterns
• Loss = Distill + 0.5·Data + μ·L1
• 2,000 epochs, patience=150
STAGE B
Structure Discovery
• Extract student's 20 drop-slot vectors
• Average across all training scenarios
• K-Means clustering (k=2..10)
• Silhouette score → optimal k*=5
• Build relation matrix R (20×5)
• R maps each step to prototypes
STAGE C
Ψ-Model Training
• Build Ψ-model with k*=5 prototypes
• Initialize from Stage B centroids
• Learnable R: softmax(logits)
• Multi-objective loss:
• Distill + Data + Initial·5 + Shape
• + 0.02·Entropy + 0.2·PhysicsMono
→
→
13/22

## Slide 14
Physics Constraints Embedded in the AI Model
7 physics constraints are hard-coded — the model structurally CANNOT violate them.
1. Sign Enforcement
ΔKL = -|d₁| ≤ 0, ΔKR = -|d₂| ≤ 0, ΔKLR = +|d₃| ≥ 0
Using -abs() and +abs() — impossible to produce wrong signs
Architectural
2. Monotonic Curves
K(t) = K⁰ + cumsum(constrained drops)
Cumulative sum of sign-enforced drops guarantees monotonicity
Architectural
3. Initial/Drop Split
Slot 1 → initial head, Slots 2-21 → drop head
Separate MLPs reflect the physical distinction
Architectural
4. Signed Log Scaling
y_log = sign(y) · log(1+|y|)
Preserves that KLR < 0 while KL, KR > 0
Preprocessing
5. Weighted Initial Loss
L_initial = 5 × MSE on step 1
First step accuracy is critical (cumsum base)
Training
6. Shape Preservation
Huber loss on first differences (Δpred vs Δtarget)
Ensures the degradation curve shape matches reality
Training
7. Physics-Monotonic Penalty
relu(ΔKL) + relu(ΔKR) + relu(-ΔKLR) × 0.2
Additional soft penalty in training loss (M8/M9)
Training
14/22

## Slide 15
Results & Performance Metrics
Overall R²
0.9891
Model explains 98.9% of variance
Curve MAPE
2.37%
Mean Abs % Error across all curves
Parameters
45,502
19.7% fewer than M6 teacher (56,646)
Test Scenarios
204
Out of 1,019 total (20% held-out)
Per-Variable Performance (M9 vs M6 Teacher)
Variable
M6 Teacher R²
M9 Ψ-NN R²
Improvement
M9 MAPE
M9 NRMSE
KL (Lateral)
0.9768
0.9905
+0.0137 ↑
2.32%
—
KR (Rotational)
0.9634
0.9796
+0.0162 ↑
2.42%
—
KLR (Cross-Coupling)
0.9690
0.9860
+0.0170 ↑
2.38%
—
Overall
0.9804
0.9891
+0.0087 ↑
2.37%
—
✦ M9 surpasses the M6 teacher on ALL variables while using 19.7% fewer parameters — the student has surpassed the teacher through structure discovery + SwiGLU gating.
15/22

## Slide 16
Full Model Comparison: M6 → M7 → M8 → M9
Metric
M6 Teacher
M7 Ψ-NN
M8 Efficient
M9 SwiGLU
Parameters
56,646
55,770
45,486
45,502
Compression
—
1.5%
19.7%
19.7%
Slot MLP
GELU 128
GELU 128
Bottleneck 48
SwiGLU 32
k* Prototypes
—
6
5
5
Relation Matrix R
—
Fixed
Learnable
Learnable
Physics Loss
—
✗
✓ λ=0.2
✓ λ=0.2
Entropy Reg.
—
✗
✓ λ=0.02
✓ λ=0.02
Overall R²
0.9804
0.9897
0.9882
0.9891
KL R²
0.9768
0.9910
0.9888
0.9905
KR R²
0.9634
0.9807
0.9780
0.9796
KLR R²
0.9690
0.9860
0.9845
0.9860
16/22

## Slide 17
Interactive Web Application & Dashboard
A Full-Featured Web Dashboard Built with Flask + Chart.js
• Real-time interactive visualization of the AI model's predictions vs real experimental data.
• Engineers can browse all 204 test scenarios, inspect per-step values, and analyze errors.
• The dashboard includes Ψ-NN structure discovery visualization, silhouette analysis, and feature importance.
📊 Prediction Charts
KL, KR, KLR curves: Target vs Predicted with error highlight
📋 Per-Step Table
Step-by-step values with % error color-coded (green < 5%, red > 20%)
🔍 Scenario Browser
Browse all 204 test cases with MAPE, R² ranking and input parameters
🧩 Ψ-NN Structure
Prototype clusters, relation matrix heatmap, silhouette analysis
⚠️ Worst-Case Diagnosis
Top-10 worst scenarios feature importance bars correlation analysis
🔬 Model Architecture
Full architecture schematic SwiGLU vs GELU comparison parameter breakdown
17/22

## Slide 18
Research Contributions & Publication Potential
1. Novel Architecture: Ψ-NN
First application of structure-discovering neural networks to geotechnical engineering. The Ψ-NN pipeline automatically finds the optimal number of prototype components.
2. SwiGLU for Scientific ML
First use of SwiGLU gating mechanism (from LLaMA/PaLM) in physics-informed models. Demonstrates that modern NLP techniques transfer to engineering domains.
3. Hard-Coded Physics
All three stiffness variables have architecturally guaranteed monotonicity. Unlike soft penalty approaches, these constraints are impossible to violate.
4. Model Compression
19.7% parameter reduction while improving accuracy (R² 0.9804 → 0.9891). The compressed student surpasses the teacher through structure discovery.
5. Interactive Digital Twin
Complete web application for real-time scenario analysis, error diagnosis, and feature importance visualization. Ready for engineering deployment.
6. Comprehensive Methodology
5 model versions (M5→M9) with systematic ablation: LSTM removal, MLP variants, learnable vs fixed R, physics loss — providing clear evidence for each design choice.
18/22

## Slide 19
Research Proposal Context (面上项目申请书)
NSFC General Program — Typhoon-Resistant OWT Foundation Design
• The research is part of a funded proposal under the NSFC
(National Natural Science Foundation of China — 面上项目 General Program).
• Research Title: AI-Driven Digital Twin for Predicting Post-Typhoon Natural
Frequency Shift in Offshore Wind Turbines with Degraded Pile Foundations
• The proposal outlines a comprehensive framework integrating:
1. Support-Condition Module (SCm): Predicts pile stiffness degradation (KL, KR, KLR)
from 8 soil/pile parameters over cyclic loading — this is what M6-M9 implements
2. Wind Turbine Module (WTm): Uses Rayleigh-Ritz analytical methods to compute
the tower+blade natural frequencies given the degraded foundation stiffness
3. Coupled Digital Twin: SCm feeds into WTm → predicts resonance risk in real-time
4. Explainable AI (XAI): Layer-wise Relevance Propagation (LRP) for interpretability
5. Uncertainty Quantification: Monte Carlo Dropout for prediction confidence bounds
• My internship contribution focuses on implementing and optimizing the SCm module
(the core AI prediction engine), which is the M6→M9 model evolution presented here.
• Reference document: 面上项目申请书撰写提纲.pdf (NSFC proposal writing outline)
19/22

## Slide 20
Timeline & Work Plan
✓
Phase 1 — Completed
Literature Review & Data Analysis
Literature review on OWT pile degradation | Study of slot attention & transformer architectures | Data preprocessing & exploration (REAL DATA.xlsx)
✓
Phase 2 — Completed
Model Development (M5 → M9)
M5: Baseline LSTM+Slot Attention (157K params) | M6: Simplified teacher (56K params, LSTM removed) | M7→M8→M9: Ψ-NN compression pipeline | SwiGLU upgrade achieving state-of-the-art (R²=0.99)
✓
Phase 3 — Completed
Web Application & Validation
Full Flask+Chart.js web dashboard | Per-scenario analysis & error diagnosis | Feature importance & worst-case identification
◐
Phase 4 — In Progress
PhD Year (Next Academic Year)
Paper writing & submission to international journal | Extend to coupled SCm+WTm Digital Twin | Add uncertainty quantification module | Implement LRP-based XAI interpretability
○
Phase 5 — Planned
Thesis & Defense
Integration of all modules into thesis | Final validation with new experimental data | PhD defense preparation
20/22

## Slide 21
Conclusion & Next Steps
✅ What Has Been Accomplished
• Developed a complete physics-informed AI system
for pile stiffness degradation prediction.
• Evolved through 5 model versions (M5 → M9),
each with clear improvements and justification.
• Final M9 model achieves:
— R² = 0.9891 (98.9% variance explained)
— 19.7% parameter compression
— Hard-coded physics guarantees
— State-of-the-art SwiGLU gating
• Built an interactive web dashboard for
real-time engineering scenario analysis.
• Produced comprehensive documentation
(LaTeX reports, architecture diagrams, code).
🚀 Next Steps (PhD Year)
• Publish research paper in an international journal:
— Target: Ocean Engineering, or Applied Ocean Research
— Content: Ψ-NN pipeline + SwiGLU for geotechnical AI
• Extend to coupled Digital Twin:
— Integrate Wind Turbine Module (WTm)
— Compute natural frequency shifts from degraded stiffness
— Predict resonance risk in real-time
• Add Explainable AI (XAI):
— Layer-wise Relevance Propagation (LRP)
— Understand which input features matter most
• Uncertainty Quantification:
— Monte Carlo Dropout for confidence bounds
— Ensemble methods for robust predictions
• Final thesis integration & defense preparation.
21/22

## Slide 22
Thank You
شكرا جزيلا • 谢谢 • Merci
Questions & Discussion
KHALIL Youssef PhD Student — Moroccan University ↔ Zhejiang University Physics-Informed AI for Offshore Wind Turbine Foundations